## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 2

## Slide 2: Where We’ve Been
Part I - Chemical Reactions
  1. Stoichiometry and Reaction Progress
  2. Reaction Thermochemistry
  3. Reaction Equilibrium
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Thermochemistry
Heat of reaction at 298 K
  Using heats of formation at 298 K
  Using heats of combustion at 298 K
Heat of reaction at other temperatures
  If there are no phase changes between 298 K and the temperature of interest
Gibbs free energy change for reaction at 298 K
Adiabatic temperature change
  If there are no phase changes between initial and final temperatures, T1 and T2

## Slide 4: Questions?

## Slide 5: Calculation of Heats of Reaction
This activity will use the 02_Activity_1_Handout.pdf file; please take it out
The handout is a solution to a problem
  It presents the calculation of the heat of the water-gas shift reaction at 250 °C
  It contains one or more mistakes
Identify as many errors as you can in the next ~5 minutes

## Slide 6: Calculation of Heats of Reaction
This activity will use the 02_Activity_1_Handout.pdf file; please take it out
The handout is a solution to a problem
  It presents the calculation of the heat of the water-gas shift reaction at 250 °C
  It contains one or more mistakes
Identify as many errors as you can in the next ~5 minutes
  You can’t arbitrarily mix heats of formation and combustion; the calculated heat at 298K is wrong.
    The heat calculated in the solution is for C + CO + O2 + H2O → 2 CO2 + H2 (if the correct values of the stoichiometric coefficients are used)
  While the proper sign convention was used, the calculation used the starting moles of reactants and final moles of products where it should have used stoichiometric coefficients.
  The calculation failed to account for the latent heat of vaporization of water upon heating from 298 to 543 K
  There may be a problem with the heat capacities: it seems odd that hydrogen is nearly equal to the carbon oxides
    Actually, the values are bad because the calculation took the first term of a polynomial expression and ignored the temperature dependent terms (you wouldn’t be expected to catch this just by looking at the calculation)
Consider how to correct the solution
  What equations would you use?
  What additional data would you need, beyond what was provided?

## Slide 7: Common Ways to Correct the Mistakes
Calculation of the heat of reaction at 298 K
  Use heats of combustion
    with liquid water as the product
    with hypothetical ideal gas water as the product
  Use heat of formation
    with same two standard states
Calculation of the heat of reaction at 543 K
  If liquid water was the standard state
  If ideal gas water was the standard state
It is essential to identify one standard state for each species and then to use that standard state consistently throughout the problem solution

## Slide 8: Heat of Reaction Trends
The three simulators provided with this unit can be used to calculate the standard heat of three different reactions at varying temperatures, pressures and compositions.
Use these simulators to explore how the standard heat of reaction is affected by changes in these variables.
Jot down any trends or relationships that you notice as you explore how the heats of reaction vary.
Summarize/Generalize Your Observations
  How did the heat of reaction vary (direction and magnitude) with
    temperature?
    pressure?
    composition?
  Will it always vary this way for every reaction?
    Why or why not

## Slide 9: What Causes the Standard Heat to Vary with T?
The standard heat of reaction does not depend upon the pressure
The standard heat of reaction does not depend upon the composition (by definition)
The standard heat of reaction at 298 K does not vary with T
The variation of the standard heat with temperature is caused by the heating and cooling steps
  Sign and magnitude are hard to predict
  Depends on number of reactants and products, relative magnitude of their heat capacities and relative magnitudes of their latent heats (if there are phase changes in the heating and cooling steps)
Stoichiometric
Amounts of the
Reactants at 298K
Stoichiometric
Amounts of the
Products at 298K
Stoichiometric
Amounts of the
Reactants at T
Stoichiometric
Amounts of the
Products at T
Heating and Cooling

## Slide 10: Where We’re Going
Part I - Chemical Reactions
  1. Stoichiometry and Reaction Progress
  2. Reaction Thermochemistry
  3. Reaction Equilibrium
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors