## Slide 1: Explore and Learn
Use KaRE TExT Equilibrium Simulators
  Set T, P and composition; click “Equilibrate”
  See thermodynamic quantities and the equilibrium composition
Use the simulator to identify as many trends as you can in the thermodynamic quantities and the equilibrium composition (as T, P and composition vary)
  Summarize your findings (what is the trend)
  Rationalize your findings (why do these changes occur in the manner they do)

## Slide 2: Are All Reactions the Same?
Compare the trends your group identified to those identified by a group studying a different reaction
  Are any of the trends different?
  Can you rationalize the combined observations of all groups, leading to some “rules of thumb”?
When the temperature increases....
When the pressure increases....
When the amount of a species present in stoichiometric excess increases....

## Slide 3: A Few Generalizations
As the temperature increases for an exothermic reaction, the equilibrium constant decreases (show why, using an equation) and so the equilibrium conversion decreases.
  The opposite is true for an endothermic reaction
As the pressure increases the equilibrium constant does not change
  For a gas phase reaction, the conversion shifts in the direction where there are fewer total moles
What others can you add?

## Slide 4: Point to Note
The equilibrium “constant” is defined using the Gibbs free energy change
The Gibbs free energy change can be related to the enthalpy and entropy changes
If the enthalpy change for the reaction and the entropy change for the reaction are taken to be approximately constant, the temperature dependence of the equilibrium constant looks very similar to the Arrhenius expression for rate coefficients (which will be introduced in the next part of the TExT)