## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 3

## Slide 2: Where We’ve Been
Part I - Chemical Reactions
  1. Stoichiometry and Reaction Progress
  2. Reaction Thermochemistry
  3. Reaction Equilibrium
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Equilibrium
Equilibrium constant
Equilibrium expression
Relating thermodynamic activities to composition
  Gases
  Liquids
  Solids

## Slide 4: Questions?

## Slide 5: Water-Gas Shift Equilibrium Analysis CO + H2O → CO2 + H2
If a system initially contains 3 moles of H2O and 1 mole of CO at 1 atm and the isobaric water-gas shift reaction proceeds to equilibrium, what is the CO conversion if the temperature is (a) 150 °C, (b) 250 °C and (c) 350 °C?
  Noting that the water-gas shift reaction is exothermic; predict whether the equilibrium conversion will increase or decrease as the temperature increases before you perform the calculations
The following expression for the heat of reaction (1) as a function of temperature and a value of -6810 cal mol-1 for ΔG0(298 K) can be generated as described in Unit 2. They are being provided here so that you can focus on the analysis of the equilibrium composition. Expressions for the heat capacities of the reagents are provided in the Table below.
Species | Ĉp (cal/(mol K) with T in K)
CO | 7.373 - 3.07 x 10-3 T + 6.662 x 10-6 T2 - 3.037 x 10-9 T3
H2O (g) | 7.701 + 4.595 x 10-4 T + 5.521 x 10-6 T2 - 0.859 x 10-9 T3
CO2 | 4.728 + 1.754 x 10-2 T - 1.338 x 10-5 T2 + 4.097 x 10-9 T3
H2 | 6.483 + 2.215 x 10-3 T - 3.298 x 10-6 T2 + 1.826 x 10-9 T3

## Slide 6: Equilibrium of Multiple Reactions Involving a Solid
In the methanation reaction, equation (1), CO and H2 are used to produce methane, with water as a byproduct. The water that is produced can then react with CO in the water-gas shift reaction, equation (2). In addition, both CO and methane can decompose to form carbon as in equations (3) and (4).
CO + 3 H2 ⇄ CH4 + H2O(v) (1)
CO + H2O(v) ⇄ CO2 + H2 (2)
2 CO ⇄ C + CO2 (3)
CH4 ⇄ C + 2 H2 (4)
Assuming that the carbon will form as graphite, the standard state for solid carbon, and that the equilibrium constants for all four reactions are known at the temperature of interest, develop the necessary equations and indicate how to use them in order to determine whether it is thermodynamically possible for carbon to form. In doing so, assume that the system initially consists of only CO and H2 in a 1:3 (CO:H2) ratio. Ideal gas behavior may be assumed.

## Slide 7: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors