## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 3

## Slide 2: Where We’ve Been
Part I - Chemical Reactions
  1. Stoichiometry and Reaction Progress
  2. Reaction Thermochemistry
  3. Reaction Equilibrium
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Equilibrium
Equilibrium constant
Equilibrium expression
Relating thermodynamic activities to composition
  Gases
  Liquids
  Solids

## Slide 4: Questions?

## Slide 5: Water-Gas Shift Equilibrium Analysis CO + H2O → CO2 + H2
If a system initially contains 3 moles of H2O and 1 mole of CO at 1 atm and the isobaric water-gas shift reaction proceeds to equilibrium, what is the CO conversion if the temperature is (a) 150 °C, (b) 250 °C and (c) 350 °C?
  Noting that the water-gas shift reaction is exothermic; predict whether the equilibrium conversion will increase or decrease as the temperature increases before you perform the calculations
The following expression for the heat of reaction (1) as a function of temperature and a value of -6810 cal mol-1 for ΔG0(298 K) can be generated as described in Unit 2. They are being provided here so that you can focus on the analysis of the equilibrium composition. Expressions for the heat capacities of the reagents are provided in the Table below.
Species | Ĉp (cal/(mol K) with T in K)
CO | 7.373 - 3.07 x 10-3 T + 6.662 x 10-6 T2 - 3.037 x 10-9 T3
H2O (g) | 7.701 + 4.595 x 10-4 T + 5.521 x 10-6 T2 - 0.859 x 10-9 T3
CO2 | 4.728 + 1.754 x 10-2 T - 1.338 x 10-5 T2 + 4.097 x 10-9 T3
H2 | 6.483 + 2.215 x 10-3 T - 3.298 x 10-6 T2 + 1.826 x 10-9 T3

## Slide 6: Water-Gas Shift Equilibrium Analysis CO + H2O → CO2 + H2
If a system initially contains 3 moles of H2O and 1 mole of CO at 1 atm and the isobaric water-gas shift reaction proceeds to equilibrium, what is the CO conversion if the temperature is (a) 150 °C, (b) 250 °C and (c) 350 °C?
Show how to calculate the value of the equilibrium constant at 298 K

## Slide 7: Water-Gas Shift Equilibrium Analysis CO + H2O → CO2 + H2
If a system initially contains 3 moles of H2O and 1 mole of CO at 1 atm and the isobaric water-gas shift reaction proceeds to equilibrium, what is the CO conversion if the temperature is (a) 150 °C, (b) 250 °C and (c) 350 °C?
Show how to calculate the value of the equilibrium constant at 298 K
Show how to calculate the value of the equilibrium constant at any other temperature, T

## Slide 8: Water-Gas Shift Equilibrium Analysis CO + H2O → CO2 + H2
If a system initially contains 3 moles of H2O and 1 mole of CO at 1 atm and the isobaric water-gas shift reaction proceeds to equilibrium, what is the CO conversion if the temperature is (a) 150 °C, (b) 250 °C and (c) 350 °C?
Show how to calculate the value of the equilibrium constant at 298 K
Show how to calculate the value of the equilibrium constant at any other temperature, T
Note, K(T) could also be calculated from ΔG(T)
  Since ΔH < 0, the second exponential will decrease as T increases, and so K will decrease

## Slide 9
Write the equilibrium expression in terms of thermodynamic activities. Then express the thermodynamic activities in terms of the mole fractions, assuming ideal gas behavior

## Slide 10
Write the equilibrium expression in terms of thermodynamic activities. Then express the thermodynamic activities in terms of moles, assuming ideal gas behavior
Express the moles in terms of the extent of reaction

## Slide 11
Write the equilibrium expression in terms of thermodynamic activities. Then express the thermodynamic activities in terms of moles, assuming ideal gas behavior
Express the moles in terms of the extent of reaction
Solve for the equilibrium extent of reaction
Calculate the equilibrium CO conversion

## Slide 12: Equilibrium of Multiple Reactions Involving a Solid
In the methanation reaction, equation (1), CO and H2 are used to produce methane, with water as a byproduct. The water that is produced can then react with CO in the water-gas shift reaction, equation (2). In addition, both CO and methane can decompose to form carbon as in equations (3) and (4).
CO + 3 H2 ⇄ CH4 + H2O(v) (1)
CO + H2O(v) ⇄ CO2 + H2 (2)
2 CO ⇄ C + CO2 (3)
CH4 ⇄ C + 2 H2 (4)
Assuming that the carbon will form as graphite, the standard state for solid carbon, and that the equilibrium constants for all four reactions are known at the temperature of interest, develop the necessary equations and indicate how to use them in order to determine whether it is thermodynamically possible for carbon to form. In doing so, assume that the system initially consists of only CO and H2 in a 1:3 (CO:H2) ratio. Ideal gas behavior may be assumed.

## Slide 13: Solution Process
Assume carbon (graphite) does form
Identify and use a mathematically independent subset of the reactions taking place
Write equilibrium expressions for those reactions
Replace the thermodynamic activities
  Express activities in terms of pressure and mole fractions
  Express mole fractions in terms of moles
  Express moles in terms of initial moles and extents of the three mathematically independent reactions
Solve the three equations for the equilibrium extents of the three mathematically independent reactions
  There may be multiple solutions
  If none of the solutions make sense (e. g. imaginary equilibrium extents of reaction), then carbon does not form, i. e. the initial assumption was not valid
If the equilibrium extents are reasonable on physical grounds, calculate the equilibrium moles of all species
  If the equilibrium moles of all species are reasonable on physical grounds, this is the equilibrium composition and carbon does form, otherwise carbon does not form

## Slide 14: Solution Process
Identify and use a mathematically independent subset of the reactions taking place
  Only 3 of the four reactions in the problem statement are mathematically independent
    See Supplemental Unit S1
    Here you can determine mathematical independence by inspection
      the first reaction is always independent
      the second reaction introduces a new reagent, CO2, so it can’t be a multiple of the first reaction
      the third reaction introduces another new reagent, C, so it can’t be a linear combination of the first two
      reaction (4) = reaction (3) - reaction (2) - reaction (1)
  Therefore, only use reactions (1) through (3) in the analysis
Write equilibrium expressions for those reactions

## Slide 15
Replace the thermodynamic activities
  Express activities in terms of pressure and mole fractions
  Express mole fractions in terms of mole

## Slide 16
  Express moles in terms of initial moles and extents of the three mathematically independent reactions
    Note that ntotal in the equations above refers to the total moles in the gas phase
      It appears as a result of substituting for the gas phase mole fraction,
    It does not include the moles of C

## Slide 17
Solve the three equations (on the last slide) for the equilibrium extents of the three mathematically independent reactions
  There may be multiple solutions
  If none of the solutions make sense (e. g. imaginary equilibrium extents of reaction), then carbon does not form, i. e. the initial assumption was not valid
If the equilibrium extents are reasonable on physical grounds, calculate the equilibrium moles of all species
  If the equilibrium moles of all species are reasonable on physical grounds, this is the equilibrium composition and carbon does form, otherwise carbon does not form

## Slide 18: Alternative Solution Steps
Assume carbon does not form
Calculate the equilibrium composition using only reactions (1) and (2)
  Check that they are independent
  Write equilibrium expressions
  Express activities in terms of pressure and mole fractions
  Express mole fractions in terms of moles
  Express moles in terms of initial moles and extents of the two reactions
  Solve the resulting equations for the equilibrium extents of reactions (1) and (2)
  Calculate the corresponding equilibrium moles (and mole fractions) of CO, H2, CH4, H2O and CO2
Write equilibrium expressions for the two carbon-forming reactions
  Rearrange them to calculate the activity of carbon, and do so
  If the resulting activity of carbon for either reaction is greater than or equal to 1, carbon does form and the initial assumption above is not valid

## Slide 19: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors