## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 4

## Slide 2: Where We’ve Been
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Unit 4 Summary
Rates
  Rate with respect to a participant species:
  Generalized rate:
  Cell growth rate:
  Specific cell growth rate:
  Relationships
Normalization of Rates
  Makes the rate an intensive quantity
  Best to normalize using the size of the location where the reaction actually occurs
    fluid volume, catalyst area, interfacial area between two fluids, etc.
Rate Expressions
  Mathematical model for net rate as a function of temperature, pressure and composition
  Single valued
  Must evaluate to zero at equilibrium values of temperature, pressure and composition

## Slide 4
Source of rate expressions
  Not from stoichiometry (except special cases to be discussed in Units 5 and 6)
  Determined experimentally
    Choose a reactor for the experiments
      Generate design equations for that reactor and validate them
    Gather experimental data that, at the minimum, span the range of the environmental variables for which the rate expression will be used
    Pick a mathematical function to be tested as a rate expression
    Substitute the rate expression into the design equations and fit the resulting equation(s) to the experimental data
    Decide whether the fit of the design equation to the data is acceptable; pick new mathematical function and iterate if it is not acceptable
Temperature dependent quantities in rate expressions
  Concentrations or partial pressures of gasses (e. g. ideal gas law)
  Equilibrium constants (recall from Unit 3)
  Rate coefficients
    Arrhenius expression is the most common model:
      Pre-exponential factor, k0,j, and activation energy, Ej, commonly found by fitting the linearized Arrhenius expression to experimentally determined values of kj at several temperatures
    Models other than the Arrhenius expression are sometimes used

## Slide 5: Questions?

## Slide 6: Effect of Stoichiometry on Reaction Rates and Extents
You will be assigned to complete one of the three handouts for today’s class and given 5 minutes to do so
All those working on handout A will come to a consensus on the correct answers and write them on the chalkboard; those working on handout B or handout C will do the same

## Slide 7: Effect of Stoichiometry on Reaction Rates and Extents
You will be assigned to complete one of the three handouts for today’s class and given 5 minutes to do so
All those working on handout A will come to a consensus on the correct answers and write them on the chalkboard; those working on handout B or handout C will do the same
All three groups were working on the same problem; the only difference is the set of stoichiometric coefficients used when writing the reaction
Compare the results
  Which are the same?
  Which are different?
    If each group had solved a kinetics problem to find the conversion after some amount of time using one of the rate expressions that differ, would the groups get the same answer or different answers?
    If you started solving a kinetics problem by writing a mole table based on the A handout and then used a generalized rate expression from the B handout, would you get the same answer as someone who used the A handout for both the mole table and the rate expression? Would someone who used the A handout for both the mole table and the rate expression get a different answer than someone who used the B handout for both the mole table and the rate expression?

## Slide 8: Arrhenius Problem Types
You have been assigned to a group of three students, and your group has been assigned one of the following problems. Set up the solution to the problem you have been assigned.
1. The rate coefficient for a reaction is 0.304 min-1 at 30 °C. The activation energy for that rate coefficient is 61.1 kJ mol-1. Assuming Arrhenius behavior, what is the rate coefficient at 65 °C?
2. If a rate coefficient doubles when the temperature is raised from 22 °C to 45 °C, what is the value of the corresponding activation energy? If the rate coefficient at 40 °C is 3.07 x 10-4 s-1, what is its value at 32 °C?
3. The rate coefficient for a particular reaction varies with temperature as follows:
T(°C) 25 35 45 55 65
103 x k, min-1 0.8 3.8 15.1 46.7 151
Determine the pre-exponential factor and the activation energy.

## Slide 9: Teach Each Other
You are now the only person in your group of three who solved your problem. Each person explain to the other two how to solve your problem.
1. The rate coefficient for a reaction is 0.304 min-1 at 30 °C. The activation energy for that rate coefficient is 61.1 kJ mol-1. Assuming Arrhenius behavior, what is the rate coefficient at 65 °C?
2. If a rate coefficient doubles when the temperature is raised from 22 °C to 45 °C, what is the value of the corresponding activation energy? If the rate coefficient at 40 °C is 3.07 x 10-4 s-1, what is its value at 32 °C?
3. The rate coefficient for a particular reaction varies with temperature as follows:
T(°C) 25 35 45 55 65
103 x k, min-1 0.8 3.8 15.1 46.7 151
Determine the pre-exponential factor and the activation energy.

## Slide 10: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors