## Slide 1: Check the Procedure
You have read a paper describing a study where a rate expression was generated.
Go through the paper and determine whether the author(s) followed the procedure given in Unit 4
  List the details of each step in the procedure such as the type of reactor selected, what data were measured, what rate expressions were tested, etc.
How would you improve the study?
  Generate a list of things that could or should be done if the study were repeated
  Identify each item as essential (to correct a mistake in the original study) or optional (to improve the results of the study)
Decide how you would rate this study: excellent, satisfactory or inadequate

## Slide 2: Points to Note
The reaction rate was not measured experimentally
  flow rates and compositions were measured
The rate expression was determined by modeling the reactor in which the reaction took place
  the reactor model includes the quantities above and it also includes the reaction rate
  therefore, the reactor model allows one to relate the experimental measurements to the rate of reaction