## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 10

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Heterogeneous Catalysis
In heterogeneous catalytic reactions, reaction is often assumed to take place at specific locations on the surface called active sites
When reactions take place on a surface, surface concentrations, not volume concentrations, are used in the rate expressions for elementary steps
  Rate and equilibrium expressions for surface reactions often use fractional coverages in place of surface concentrations
  The total surface concentration of sites, Csites, is incorporated into the pre-exponential factor of the rate coefficient
Active sites are usually assumed to be conserved
Simplifications may be possible if one species is the most abundant surface intermediate (masi):
Langmuir-Hinshelwood kinetics are a common type of rate expression for heterogeneous catalytic reactions results when
  A surface reaction step is assumed to be rate-determining
  All of the adsorption/desorption steps are quasi-equilibrated

## Slide 4: Questions?

## Slide 5: Activity 10.1
The water-gas shift reaction, equation (1), might take place according to the mechanism given in equations (2) and (3). If step (3) is irreversible, find an expression for the rate of water-gas shift in terms of the partial pressures of the stable species (and rate and equilibrium constants).
Overall, macroscopically observed reaction:
CO + H2O ⇄ CO2 + H2 (1)
Postulated mechanism:
CO + O−❋ ⇄ CO2 + ❋ (2)
H2O + ❋ ⇄ H2 + O−❋ (3)
We will solve this problem as a relay race. When told to start, one group member should go to the board and write one equation needed to solve the problem, then sit down. The next member should then go to the board and either correct an existing equation or write an additional one. The first group to list all necessary equations correctly and indicate how to solve them wins!

## Slide 6: Activity 10.2
The oxidation of carbon monoxide is given in equation (1) below. Suppose that the mechanism is given by equations (2) through (4) and that step (4) is rate-limiting. Derive a rate expression in terms of only the partial pressures of the reagents and constants. How does the result change if O−✳ is the most abundant surface intermediate? Comment upon the resulting rate expression.
Overall, macroscopically observed reaction:
2 CO + O2 ⇄ 2 CO2 (1)
Postulated mechanism:
O2 + 2 ✳ ⇄ 2 O−✳ (2)
CO + ✳ ⇄ CO−✳ (3)
CO−✳ + O−✳ ⇄ CO2 + 2 ✳ (4)

## Slide 7: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
    4. Reaction Rates and Temperature Effects
    5. Empirical and Theoretical Rate Expressions
    6. Reaction Mechanisms
    7. The Steady State Approximation
    8. Rate Determining Step
    9. Homogeneous and Enzymatic Catalysis
    10. Heterogeneous Catalysis
  B. Kinetics Experiments
    11. Laboratory Reactors
    12. Performing Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors