## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 11

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
    11. Laboratory Reactors
    12. Performing Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Laboratory Reactors
Three models for laboratory reactors used to generate kinetics data when only one reaction is taking place
  Isothermal batch reactor
    Critical assumptions are perfect mixing and isothermal
  Steady state CSTR
    Critical assumptions are steady state and perfect mixing
  Isothermal, isobaric, steady state plug flow reactor
    Critical assumptions are plug flow, steady state, isothermal and isobaric
The validity of the model equations must be tested before kinetics data are generated and analyzed
  Some tests don’t require reaction to be occurring
    Flow visualization (smoke tests), extensive instrumentation, measurement of the age function
  Other tests can be performed while reaction takes place
    Unit 12

## Slide 4: Testing Using the Age Function
Apply a stimulus at the inlet to the reactor and measure the response at the outlet from the reactor
  Stimulus may be step change or impulse change in the concentration of a tracer
    Tracer is something that flows exactly the same as the fluid, but is easily distinguished
    The stimulus is applied at a point in time, t0
  Response is the change in concentration of the tracer in the fluid leaving the reactor over time (after application of the stimulus)
F(λ) ≡ fraction of the fluid leaving a flow system that has been inside the system for a period of time < λ
  F(0) = 0
  F(∞) = 1
Calculation of the age function
  Using a step change stimulus:
  Using an impulse stimulus:
    If the mass of tracer in the impulse was not measured:

## Slide 5: Testing Using the Age Function
Expected age functions for reactors that obey the assumptions of the ideal reactor models
  CSTR:
  PFR:
Plot F(λ) vs. λ and FCSTR(λ) (or FPFR(λ)) vs. λ on the same axes
Agreement between the measured age function and the ideal reactor age function is a necessary, but not sufficient criterion
  It confirms that the time scale for mixing is much shorter than the residence time in the reactor
  It can fail if the time scale for reaction is much shorter than the time scale for mixing

## Slide 6: Questions?

## Slide 7: Activity 11.1
Consider a plug flow reactor that you want to be isothermal
  It’s essentially a tube
  You can add or remove heat through the walls
    for example, you could flow steam over the outside of the tube to add heat
The amount of heat released at any point along the reactor is proportional to the rate at that point
  At the inlet, where the reactant concentration is high, the rate will be high, and lots of heat will be released
  Farther along the reactor, where the reactant concentration is smaller, the rate will not be as large, and less heat will be released.
  In other words, the amount of heat that needs to be removed changes continually along the length of the reactor
How, then, can you configure the system so the reactor is isothermal?
  If you remove enough heat to cool the inlet to the desired isothermal temperature, then farther down the reactor, the temperature will be below the desired value because too much heat is being removed.
The same problem occurs with a batch reactor except that there you need to remove more heat at the start of the experiment and less heat later in the experiment
  How would you do this?

## Slide 8: Activity 11.1
Reactant Concentration High
Rate High
Large Heat Release
Reactant Concentration Lower
Rate Lower
Smaller Heat Release
....

## Slide 9: Conclusions
It can be difficult to actually operate a reactor isothermally
  Need a thermal sink or reservoir
    Reactor immersed in a stirred oil bath or a fluidized sand bath
    Reactor tightly fitted within a large block of a metal with a high thermal conductivity (e. g. Al)
      Metal block heated via oil bath, electrical resistance heaters, etc.
For this reason, most commercial reactors do not operate isothermally

## Slide 10: Activity 11.2
In this activity you will use one of the stimulus-response simulators provided with Unit 11 to perform a virtual stimulus-response experiment, and then you will analyze the data you generate and decide whether or not the reactor you studied can be modeled as an ideal CSTR or an ideal PFR
Points you should consider
  How do you pick the conditions for the experiment?
  How long after the application of the stimulus should you continue to collect response data?

## Slide 11: Activity 11.2
In this activity you will use one of the stimulus-response simulators provided with Unit 11 to perform a virtual stimulus-response experiment, and then you will analyze the data you generate and decide whether or not the reactor you studied can be modeled as an ideal CSTR or an ideal PFR
Points you should consider
  How do you pick the conditions for the experiment?
    The conditions should be as close as possible to those that will be used when running the planned reaction
    The conditions should yield stimulus response data that can be accurately analyzed
      e. g, you wouldn’t want the entire response to take place within a microsecond
      You want a tracer level that is substantially greater than the experimental noise associated with measuring the tracer concentration
  How long after the application of the stimulus should you continue to collect response data?
    For a step change stimulus
      Eventually one expects the outlet tracer concentration to equal the inlet concentration
      Therefore collect data until this occurs
    For an impulse stimulus
      Eventually one expects all the tracer in the impulse to come out of the reactor
      Collect data until you see the tracer concentration increase and then decrease back until the inlet and outlet concentrations are equal
        This could fail if the tracer comes out in two “batches” that are separated in elution time

## Slide 12: Data Workup
Calculate the age function for each outlet composition measurement
  Step change stimulus:
  Impulse stimulus:
Plot the corresponding ideal reactor age function
  CSTR:
  PFR:
Plot the data points from point 1 on the same axes and compare
  Remember, if the points fall on the line, that is a necessary, but not sufficient result for treating the reactor as being ideal

## Slide 13: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
    11. Laboratory Reactors
    12. Performing Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors