## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 12

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
    11. Laboratory Reactors
    12. Performing Kinetics Experiments
  C. Analysis of Kinetics Data
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Testing Reactor Models
If mixing is perfect, the rate of reaction should not depend upon agitator speed
Interfacial Gradients
  The ideal reactor models assume locally uniform composition
  When two phases coexist, concentration and/or temperature gradients develop near the interface between the phases
    Gradients between the bulk fluid and the surface can cause external transport limitations
    Gradients within the pores of a solid can cause internal transport limitations
  Experimental and computational tests can be performed to make sure the rate is negligibly affected by these gradients
External transport limitation tests
  The conversion should not vary with linear flow velocity if the residence time is constant
    At very low flow rates this test lacks sensitivity
  Be suspicious of first order kinetics with very low activation energies

## Slide 4: Testing for Transport Limitations and Performing Kinetics Experiments
Computational tests for external transport limitations
Experimental test for internal transport limitations
  For fixed residence time, the conversion should not vary as a function of catalyst particle size
  For fixed dispersion of supported catalysts, the conversion should not vary with catalyst loading
  Be suspicious if the activation energy drops by 50% at higher temperatures
Computational tests for internal transport limitations
Typical kinetics experiments
  Batch reactor: charge and bring to temperature, measure initial composition
    measure composition vs. time
    several data points per experiment
  Flow reactors: set inlet conditions and temperature, wait until system is at steady state
    measure outlet composition
    one data point per experiment

## Slide 5: Kinetics Experiments
Three possible objectives
  Determine whether the reaction is reversible by attempting to attain 100% conversion of the limiting reagent
  Conduct a few experiments where “base conditions” are selected and concentration of each reagent is changed holding all others constant
    Results can help when guessing a rate expression to test
  Gather data that span all possible temperatures and compositions of interest for the resulting rate expression
Experimental approach
  Operate the reactor in the preferred mode to simplify data analysis
  Conduct experiments in constant temperature blocks
    Analyze data in two steps: first by block to get rate coefficient(s) at each block temperature
    Then analyze rate coefficients vs. block temperatures to get Arrhenius parameters
  Consider statistical design of experiments

## Slide 6: Questions?

## Slide 7: Activity 12.1 Four Slide Presentation
Units 11 and 12 presented a number of different procedures for “testing” laboratory reactors. Prepare a four slide presentation that summarizes the important information. You can simply sketch out your slides on paper; you do not need to actually prepare slides (you may, if you wish).
The recommended format for the presentation is to use the first slide to describe why the tests are necessary and what they actually test. The remaining three slides should be devoted to actual tests, organized in some logical order.
A few of you may be called upon to show your slides and describe the points you would seek to make with each slide.

## Slide 8: Activity 12.2
Example 12.5 indicated that there are differences between the kinetics data generated using a batch reactor and those generated using a CSTR
  There are also differences in the experiments used to generate the data
In this activity, the nature of these differences will be observed using kinetics simulators for a batch reactor and a CSTR
  Apart from batch versus continuous, what experimental aspects are different?
  How can these differences be rationalized without resorting to equations?
  What implications might these differences have upon the data analysis?
As you work, you should copy your simulator results to the Excel handout 12_Activity_2.xlsx
  As you work through the activity, you will enter simulator results in cells that are colored green
  As you fill in those results, values will appear in cells colored yellow and blue
Generation of batch reactor kinetics data using a single experiment
  Set T = 340 ºC, V = 5 L, CA = CB = 1.0 M and CX = CY = 0.0 M
  Start the experiment and watch the concentration of Y
    Record a data point when CY is approximately 0.2, 0.4, 0.6, 0.8 and 0.9 M
    Note any trends you observe
  Fill in the results in the cells of the batch reactor table (top, left) that are colored light green

## Slide 9
Generate CSTR data using the same feed composition and reaction times
  The upper CSTR data table on the spreadsheet should be pre-filled in except for the last two columns
    Each row is a separate CSTR experiment
    The feed composition for every experiment is the same as the initial composition in the batch experiment; the temperatures are the same, as well
    The feed flow rates have been filled in for you so that the CSTR residence times are equal to the elapsed times for your five batch reactor experiments
  Use the CSTR simulator to perform the 5 experiments using the settings in the table
    Record the outlet temperature and concentration of Y for each experiment in the spreadsheet
  Note any trends you observe
  Note any differences you observe between the batch experiment or data and the CSTR
Generate alternative CSTR data where the CSTR feed composition equals the batch reactor composition at the start of a batch reactor interval and the residence time in the CSTR equals the length of the batch reactor interval
  The lower CSTR data table on the spreadsheet should again be pre-filled in except for the last two columns
  Note, in this series of experiments, the CSTR feed simulates the batch reactor composition at the start of each of the five sampling intervals
    The CSTR feed rate has been calculated so that the CSTR residence time is equal to the elapsed time until the next batch reactor sample was taken
  As above, use the CSTR simulator to perform the 5 experiments using the settings in the table
  Note any trends and and differences between the batch experiment or data and the CSTR

## Slide 10: Procedure Summary
Generation of batch reactor kinetics data using a single experiment
  Set T = 340 ºC, V = 5 L, CA = CB = 1.0 M and CX = CY = 0.0 M
  Start the experiment and watch the concentration of Y
    Record a data point when CY is approximately 0.2, 0.4, 0.6, 0.8 and 0.9 M
    Note any trends you observe
  Fill in the results in the cells of the batch reactor table (top, left) that are colored light green
Generate CSTR data using the same feed composition and reaction times
  Use the CSTR simulator to perform the 5 experiments using the settings in the upper CSTR table
    Record the outlet temperature and concentration of Y for each experiment in the spreadsheet
  Note any trends you observe
  Note any differences you observe between the batch experiment or data and the CSTR
Generate alternative CSTR data
  As above, use the CSTR simulator to perform the 5 experiments using the settings in the lower CSTR table
    Record the outlet temperature and concentration of Y for each experiment in the spreadsheet
  Note any trends you observe
  Note any differences you observe between the batch experiment or data and the CSTR

## Slide 11: Discuss and Rationalize
List trends you observed in the batch experiment and data
  Offer a qualitative explanation for the trend; you may not use an equation to explain the trend
List trends you observed in the CSTR experiment and data
  Offer a qualitative explanation for the trend; you may not use an equation to explain the trend
List the differences you observed between the batch experiment/results and the CSTR experiment/results
  Offer a qualitative explanation for the differences
  Discuss what implications the differences might have upon the use of the data for the testing of a rate expression
Can you think of a way to eliminate the differences between the two sets of data?

## Slide 12: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
    11. Laboratory Reactors
    12. Performing Kinetics Experiments
  C. Analysis of Kinetics Data
    13. CSTR Data Analysis
    14. Differential Data Analysis
    15. Integral Data Analysis
    16. Numerical Data Analysis
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors