## Slide 1: Generation of Kinetics Data Using a CSTR
Suppose you have been tasked with generating a rate expression for the reaction A + B → Y + Z
  Y is a new compound discovered by your research department, and thermodynamic data for it are not available
  The company wants to build a pilot plant for this reaction
    The reactor could operate anywhere in the temperature range from 310 to 350 K range
    The concentrations of the reagents will be 5 M or less
Design a set of experiments to generate the kinetics data using a 100 L CSTR that can operate at temperatures from 270 to 360 K with flow rates up to 1000 L/min
Use the IsoCSTR simulator to perform the experiments and generate the kinetics data
Recall three objectives
  Determine the reversibility of the reaction
  Initial scoping experiments
    Set base conditions, then systematically change only one concentration from the base case
  Comprehensive data set spanning possible range of temperature and composition where the rate expression might be used
    Collect data in constant temperature blocks

## Slide 2: Design of Experiments
To gauge reversibility of the reaction
  2 experiments
    One at low temperature (298 K) and one at high temperature (360 K)
    High concentrations of products (CY = CZ = 1.0 M) and low concentrations of reactants (CA = CB = 0.1 M)
    Low flow rate (high space time) to get highest conversion possible
  Results
    To within the experimental noise, no product was converted to reactant
    The reaction is irreversible
To scope composition dependence we want to double one concentration while holding the rest constant
  Problem: we set the inlet concentrations, not the outlet concentration
    If the space time is high, all of the concentrations will be considerably different at the outlet than they were at the inlet
    Therefore, use a small space time so that the concentrations change only slightly
  5 experiments, all at the same temperature (325 K) and lowest allowed flow (5 L/min)
    Base case inlet composition: CA = CB = CY = CZ = 1 M
      Outlet CY is 1.06 M, so concentration changes are small
  Results
    Double inlet CA or CB, ΔCY is approximately double the base case
    Double inlet CY or CZ, ΔCY is approximately the same as the base case
    r = k CA CB may be a good first guess for the rate expression

## Slide 3: Design of Experiments
Large data set spanning conditions of interest
  Five “blocks” of experiments, e. g. at 305, 320, 330, 345, 355 K
  Within each block span a range of concentrations of each reagent by
    Using different feed compositions
    Varying space time
  A statistical design is preferred
    I just randomly selected different inlet settings trying to span the range of concentrations
      Arbitrarily picked inlet concentrations then did a few experiments with different flow rates
      Repeated with a second set of inlet concentrations
Based upon results, you can always adjust plan as you go
  Some variables may have no effect or lead to negligible conversion
  You can always go back and perform additional experiments