## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 15

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
    13. CSTR Data Analysis
    14. Differential Data Analysis
    15. Integral Data Analysis
    16. Numerical Data Analysis
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Integral Data Analysis
Distinguishing features of integral data analysis
  The model equation is a differential equation
  The differential equation is integrated to obtain an algebraic equation which is then fit to the experimental data
Before it can be integrated, the differential model equation must be re-written so the only variable quantities it contains are the dependent and independent variables
  For a batch reactor, ni and t
  For a PFR, ṅi and z
  Be careful with gas phase reactions where the number of moles changes
    P and ntot (in a batch reactor) or and ṅtot (in a PFR) will be variable quantities
Often the integrated form of the PFR design equation cannot be linearized
  Use non-linear least squared (Unit 16)
  If there is only one kinetic parameter
    Calculate its value for every data point
    Average the results and find the standard deviation
    If the standard deviation is a small fraction of the average and if the deviations of the individual values from the average are random
      The model is accurate
      The average is the best value for the parameter and the standard deviation is a measure of the uncertainty

## Slide 4: Half-life Method
Useful for testing rate expressions that depend, in a power-law fashion, upon the concentration of a single reactant
The half-life, t1/2, is the amount of time that it takes for the concentration of the reactant to decrease to one-half of its initial value.
The dependence of the half-life upon the initial concentration can be used to determine the reaction order, α
  if the half-life does not change as the initial concentration of A is varied, the reaction is first order (α = 1)
  otherwise, the half-life and the initial concentration are related
    the reaction order can be found from the slope of a plot of the log of the half-life versus the log of the initial concentration

## Slide 5: Questions?

## Slide 6: Activity 15.1
A rate expression is needed for the reaction A → Y + Z, which takes place in the liquid phase. It doesn’t need to be highly accurate, but it is needed quickly. Only one experimental run has been made, that using an isothermal batch reactor. The reactor volume was 750 mL and the reaction was run at 70 °C. The initial concentration of A was 1M, and the concentration was measured at several times after the reaction began; the data are listed in the table on the right.
Find the best value for a first order rate coefficient using the integral method of analysis.
t (min) | CA(M)
1 | 0.874
2 | 0.837
3 | 0.800
4 | 0.750
5 | 0.572
6 | 0.626
7 | 0.404
8 | 0.458
9 | 0.339
10 | 0.431
12 | 0.249
15 | 0.172
20 | 0.185

## Slide 7: Activity 15.2
The gas phase, isothermal decomposition shown in reaction (1), was studied at 1150 K and 1 atm pressure using a PFR.
  2 A → 2 Y + Z (1)
The feed was pure A, and the tubular reactor had a volume of 150 cm3. The inlet flow rate was varied and the outlet partial pressure of Z was measured. The data are tabulated in the table to the right.
Group 1: Test the adequacy of rA = −k⋅CA as a rate expression.
Group 2: Test the adequacy of rA = −k⋅CA2 as a rate expression.
Inlet Feed Rate (cm3 min-1) | Outlet Mole Fraction of Z
2.26 | 0.088
1.23 | 0.131
0.73 | 0.166
0.51 | 0.195
0.29 | 0.228
0.17 | 0.260
0.09 | 0.287
Notes: three groups at board solving; three groups in seats solving, seats check answer of board, go over solutions.

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
  A. Rate Expressions
  B. Kinetics Experiments
  C. Analysis of Kinetics Data
    13. CSTR Data Analysis
    14. Differential Data Analysis
    15. Integral Data Analysis
    16. Numerical Data Analysis
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors