## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 17

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
    17. Reactor Models and Reaction Types
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Engineering
Objectives
  Construct accurate mathematical models of real world reactors
  Use those models to perform some engineering task
Tasks
  Reaction engineering: studies involving an existing reactor
  Reactor design: specifying a reactor that doesn’t yet exist along with its operating procedures
Real world reaction engineering
  Maximize the rate of profit realized by operating the overall process (not just the reactor)
  Integration of the reactor into the overall process may place constraints upon the reactor design and operating conditions
Generally
  generate the desired product as fast as possible
  with the highest selectivity possible
  using as little energy as possible
  in as small a reactor volume as possible
  while maintaining
    reliability
    operability
    environmental compatibility
    safety

## Slide 4: Ideal Reactor Design Equations
Batch Reactor
CSTR

## Slide 5: Ideal Reactor Design Equations
Steady State CSTR
PFR

## Slide 6: Ideal Reactor Design Equations
Steady State RFR
(Unpacked Tube)
(Packed Bed)

## Slide 7: Typical Kinetics Behavior and Reaction Classification
Typical kinetics behavior
  As T increases, the rate increases
    final conversion decreases for exothermic; increases for endothermic reactions
  As concentration or partial pressure of reactants decreases, the rate decreases
  As the concentration or partial pressure of products increases, the rate decreases for reversible reactions; is not strongly affected for irreversible reactions
Reaction Classification
  Auto-thermal reactions: the (exothermic) heat of reaction is sufficiently large to heat the reactants to reaction temperature
  Auto-catalytic reactions: rate increases as the product concentration increases
  Reactant Inhibited Reactions: rate decreases as the reactant concentration increases
  Product Inhibited Reactions: rate decreases as the product concentration increases
  Parallel Reactions
    A → B
    A → C
  Series Reactions
    A → B
    B → C
  Series-Parallel Reactions
    A + B → R + S
    R + B → T + S

## Slide 8: Questions?

## Slide 9: Activity 17.1
Liquid phase reactions (1) and (2) below take place in an adiabatic batch reactor.
A + B ⇄ R + S (1)
R ⇄ T + U (2)
The initial temperature of the 2 m3 reactor is 450 K and it initially contains 3.5 kmol m−3 each of A and B (the only species present). Heat capacities of the species, in cal mol−1 K−1, are as follows: A = 7.5, B = 8.5, R = 9.3, S = 12.1, T = 5.7, and U = 6.3. The reactions are elementary with rate coefficients as given below.
k1 = (8.3 x 10−2 m3 kmol−1 s−1) exp{−(18,000cal mol−1)/(RT)} (3)
k2 = (3.7 x 10−3 s−1) exp{−(13,500cal mol−1)/(RT)} (4)
The reactions are irreversible with ΔH1(298 K) = −9870 cal mol−1 and ΔH2(298 K) = −8700 cal mol−1. How long will it take for the concentration of S to reach 2.5 kmol m−3?
Write the mole and energy balance design equations for this system, expanding all sums and continuous products

## Slide 10
Mole balance on A
Other mole balances
Energy balance

## Slide 11: Activity 17.2
Aqueous phase reactions (1) and (2) below take place in an adiabatic CSTR operating at steady state.
A + B ⇄ R + S (1)
A + B ⇄ T + U (2)
The feed to the 2 m3 reactor is at 78ºC and it initially contains A and B at equal 1.5 M concentrations. The heat capacity of the solution may be taken to equal that of water, 1 cal g-1. The reactions are elementary with rate coefficients as given below.
k1 = (8.3 x 10−2 m3 kmol−1 s−1) exp{−(8,000cal mol−1)/(RT)} (3)
k2 = (4.7 x 10−2 m3 kmol−1 s−1) exp{−(12,000cal mol−1)/(RT)} (4)
The reactions are irreversible with ΔH1(298 K) = 9870 cal mol−1 and ΔH2(298 K) = 8700 cal mol−1. Heat is added to the reactor by passing saturated steam at 120ºC through a coil with an area of 0.7 m2 that is submerged in the solution. The overall heat transfer coefficient is 25 BTU h-1 ft-2 ºF
Write the mole and energy balance design equations for this system, expanding all sums and continuous products

## Slide 12
Mole balance on A
Other mole balances
Energy balance

## Slide 13: Activity 17.3
Suppose the steam being fed to the submerged coil was suddenly changed to saturated steam at 100ºC, write the design equations needed to model the reactor.
Before the steam temperature changed, the system was at steady state
  The volumetric flow rate was not changing with time
  The reaction volume was not changing with time
  The inlet molar flow rates were not changing with time
  The outlet molar flow rates were not changing with time
  The temperature was not changing with time
  The pressure was not changing with time
Which of these quantities will change with time after the steam temperature changes?

## Slide 14: Activity 17.3
Suppose the steam being fed to the submerged coil was suddenly changed to saturated steam at 100ºC, write the design equations needed to model the reactor.
Before the steam temperature changed, the system was at steady state
Which of these quantities will change with time after the steam temperature changes?
  The volumetric flow rate was not changing with time - remains constant
  The reaction volume was not changing with time - remains constant
  The inlet molar flow rates were not changing with time - remains constant
  The outlet molar flow rates were not changing with time - will change over time
  The temperature was not changing with time - will change over time
  The pressure was not changing with time - remains constant
What terms must be added to the mole balance on A?

## Slide 15: Activity 17.3
Which of these quantities will change with time after the steam temperature changes?
  The volumetric flow rate was not changing with time - remains constant
  The reaction volume was not changing with time - remains constant
  The inlet molar flow rates were not changing with time - remains constant
  The outlet molar flow rates were not changing with time - will change over time
  The temperature was not changing with time - will change over time
  The pressure was not changing with time - remains constant
What terms must be added to the mole balance on A?
  previous steady state balance on A:
  general non-steady state balance:
  new balance on A:
What terms must be added to the energy balance?

## Slide 16: Activity 17.3
Which of these quantities will change with time after the steam temperature changes?
  The volumetric flow rate was not changing with time - remains constant
  The reaction volume was not changing with time - remains constant
  The inlet molar flow rates were not changing with time - remains constant
  The outlet molar flow rates were not changing with time - will change over time
  The temperature was not changing with time - will change over time
  The pressure was not changing with time - remains constant
What terms must be added to the energy balance?
0
0

## Slide 17: Where Were Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
    17. Reactor Models and Reaction Types
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors