## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 19

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Engineering with Batch Reactors
Operation
  Clean
  Prepare and Charge
  Process according to Protocol
  Drain
Productivity
  Turnaround time
  Processing (reaction) time
Reactor Design Problems
  Sizing and Processing Protocol
  Optimization
Other Reaction Engineering Tasks
  Simulate the entire process (e. g. for automating controls)
  Evaluate the effect of some change in the protocol
Reasons for using Batch Reactors
  Flexibility
  Small Quantities of Product
  Precise Control
Disadvantages
  Labor Intensive
  Batch to Batch Consistency
  Not Suited to Producing Large Quantities
Importance of Physical Understanding
  You will retain your physical understanding much longer than an equations-based understanding
  A physical understanding may allow you to eliminate some design alternatives without having to solve the design equations
  It will be easier to make creative new (patentable) discoveries if you have a sound physical understanding

## Slide 4: Methodology of Qualitative Batch Reactor Analysis
Consider a small interval of time at the start of the reaction
  Determine how concentrations and temperature will change during that interval
  Determine whether the net effect of the changes will be a rate that is larger or smaller
  Determine the effect of these changes upon the equilibrium conversion
Consider the next interval of time
  Determine how concentrations and temperature will change during that interval
    If the rate is larger than the previous interval, changes will be larger
    If the rate is smaller than the previous interval, changes will be smaller
Knowing that eventually the rate will go to zero as the system approaches equilibrium
  Decide whether the pattern established in the early intervals can continue
  If the early pattern can’t continue, infer what must happen so that the system approaches equilibrium properly

## Slide 5: Questions?

## Slide 6: Analysis of a Reactant-Inhibited Reaction
Suppose the catalytic reaction (1) below is reactant inhibited with a rate expression of the form shown in equation (2). The reaction is irreversible, and K is very, very small in magnitude. Predict how the rate and the conversion will vary as a function of batch reaction time (a) if PA0 = PB0, (b) if PA0 > PB0 and (c) if PA0 < PB0.
A + B → Y + Z (1)
(2)

## Slide 7: Analysis of a Reactant-Inhibited Reaction
Suppose the catalytic reaction (1) below is reactant inhibited with a rate expression of the form shown in equation (2). The reaction is irreversible, and K is very, very small in magnitude. Predict how the rate and the conversion will vary as a function of batch reaction time (a) if PA0 = PB0, (b) if PA0 > PB0 and (c) if PA0 < PB0.
A + B → Y + Z (1)
(2)
(a) Initially the rate will not change over time because K is negligible and PA and PB cancel out; the conversion will increase linearly
- at some point, the K in the denominator will become significant so that the numerator decreases more than the denominator and the rate will start to decrease more and more (concave down); as a consequence, the conversion versus time will become concave downward (the slope will become increasingly shallow)
- the rate versus time must eventually pass through an inflection point (become concave upward) and asymptotically approach a value of zero; this will occur as the K in the denominator becomes predominant; but the conversion will remain concave downward, approaching a horizontal asymptote as time goes to infinity.

## Slide 8: Analysis of a Reactant-Inhibited Reaction
Suppose the catalytic reaction (1) below is reactant inhibited with a rate expression of the form shown in equation (2). The reaction is irreversible, and K is very, very small in magnitude. Predict how the rate and the conversion will vary as a function of batch reaction time (a) if PA0 = PB0, (b) if PA0 > PB0 and (c) if PA0 < PB0.
A + B → Y + Z (1)
(2)
(b) Here we’ll assume that A is in sufficient excess that the denominator is nearly constant over the course of the reaction. In that case, the reaction is effectively first order in B. The conversion will start at zero with a positive slope. That slope will decrease over time, eventually reaching zero as the time approaches infinity. The rate will start with a finite positive value and a negative slope; the slope will increase (i. e. become less negative) over time until it eventually reaches zero as the time approaches infinity.
(c) The rate expression cannot be valid for this case since it predicts a positive rate when there is no A present. As a result, it would be meaningless in this case to predict the qualitative behavior of a reactor on the basis of this rate expression.

## Slide 9: Qualitative Analysis with Parallel Reactions
Suppose irreversible, parallel reactions (1) and (2) take place isothermally in a batch reactor with kinetics as indicated. Prepare a three slide presentation that describes and qualitatively justifies approaches you might employ in order to improve the selectivity for D.
A + S → D r = 10 e-10/T CA CS (1)
A + S → U r = 10 e-15/T CA (CS)2 (2)

## Slide 10: Qualitative Analysis with Parallel Reactions
Suppose irreversible, parallel reactions (1) and (2) take place isothermally in a batch reactor with kinetics as indicated. Prepare a three slide presentation that describes and qualitatively justifies approaches you might employ in order to improve the selectivity for D.
A + S → D r = 10 e-10/T CA CS (1)
A + S → U r = 10 e-15/T CA (CS)2 (2)
Instantaneous selectivity parameter:
  D is favored by
    low temperature
    low CS
  Low reaction temperature will trade off rate of conversion versus selectivity to D; use the lowest acceptable temperature
  Low initial concentration of S will trade off conversion and time per batch versus selectivity to D
Other approaches
  Find a catalyst that favors production of D
  If reaction is solution phase, find a solvent that favors production of D

## Slide 11: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors