## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 19

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Modeling a Process Step for a Batch Reactor
Write a mole balance design equation for every reactant and product
Write an energy balance
  May not be needed if the reactor operates isothermally
If there is heat transfer to a heat transfer fluid of uniform temperature
  set in the energy balance
  If the heat is from a heat transfer fluid’s phase change, check that the flow rate of the heat transfer fluid is at least equal to the minimum value
    determine the proper value of U based upon geometry, etc.
  If the heat is sensible heat from heat transfer fluid that is perfectly mixed, write an energy balance on the heat transfer fluid
    set in both energy balances
    determine the proper value of U based upon geometry, etc.
Solve the resulting set of design equations

## Slide 4: Simplifications and Solution
Simplification of the energy balance on the reaction volume
  If the reactor is adiabatic, the heat term equals zero
  The work term almost always equals zero (no shafts or moving boundaries except agitator)
  The derivative of the volume with respect to time may almost always be set equal to zero
  The derivative of the pressure with respect to time
    may almost always be set to zero for liquids
    is re-written using the ideal gas law (for ideal gases)
Numerical solution of the set of design equations (initial value ordinary differential equations)
  Write the equations in the following (vector) form:
  Use software of your choice to solve numerically; no matter what software you use you will need to provide
    the initial values of the dependent variables, that is, the values of each yi at t = 0
    the final value of either t or one of the dependent variables
    code that evaluates each of the functions, fi, given a value for t, values for each of the dependent variables, yi, and information given in the problem specification and other reference sources such as handbooks

## Slide 5: Questions?

## Slide 6: Activity 19.1
A gas mixture contains 1500 ppm of A, 1000 ppm of B and 7% C. The remainder of the gas is inert (non-reactive). A 3 L reactor steel reactor is charged with this mixture at 1115 K and 1.7 atm. Reactions (1) and (2) take place adiabatically with rates given by equations (3) and (4). The pre-exponential factors for reactions (1) and (2) are 6.1 x 1016 L mol-1 s-1 and 5.5 x 1013 s-1, respectively; the activation energies are 250 and 320 kJ/mol, respectively. Calculate the parts per million of B after 0.5, 1 and 5 seconds. You may assume the heats of reactions (1) and (2) to be constant and equal to -1700 kJ/mol and -800 kJ/mol, respectively. The heat capacities of the gases may be taken to equal that of the inert, 32 J mol−1 K−1, and to be independent of temperature.
4 A + 4 B + C → 4 Y + 6 Z (1)
4 A + 5 C → 4 B + 6 Z (2)
(3)
(4)

## Slide 7: Activity 19.2
Many mathematics programs provide code that can solve sets of ODEs written in the form
  M is called the mass matrix
Reformulate the design equations for Activity 19.1 in this form
  Starting with this set of equations
  Add a seventh equation from the ideal gas law
  Write out the mass matrix and the functions, f

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors