## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 19

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Modeling a Process Step for a Batch Reactor
Write a mole balance design equation for every reactant and product
Write an energy balance
  May not be needed if the reactor operates isothermally
If there is heat transfer to a heat transfer fluid of uniform temperature
  set in the energy balance
  If the heat is from a heat transfer fluid’s phase change, check that the flow rate of the heat transfer fluid is at least equal to the minimum value
    determine the proper value of U based upon geometry, etc.
  If the heat is sensible heat from heat transfer fluid that is perfectly mixed, write an energy balance on the heat transfer fluid
    set in both energy balances
    determine the proper value of U based upon geometry, etc.
Solve the resulting set of design equations

## Slide 4: Simplifications and Solution
Simplification of the energy balance on the reaction volume
  If the reactor is adiabatic, the heat term equals zero
  The work term almost always equals zero (no shafts or moving boundaries except agitator)
  The derivative of the volume with respect to time may almost always be set equal to zero
  The derivative of the pressure with respect to time
    may almost always be set to zero for liquids
    is re-written using the ideal gas law (for ideal gases)
Numerical solution of the set of design equations (initial value ordinary differential equations)
  Write the equations in the following (vector) form:
  Use software of your choice to solve numerically; no matter what software you use you will need to provide
    the initial values of the dependent variables, that is, the values of each yi at t = 0
    the final value of either t or one of the dependent variables
    code that evaluates each of the functions, fi, given a value for t, values for each of the dependent variables, yi, and information given in the problem specification and other reference sources such as handbooks

## Slide 5: Questions?

## Slide 6: Activity 19.1
A gas mixture contains 1500 ppm of A, 1000 ppm of B and 7% C. The remainder of the gas is inert (non-reactive). A 3 L reactor steel reactor is charged with this mixture at 1115 K and 1.7 atm. Reactions (1) and (2) take place adiabatically with rates given by equations (3) and (4). The pre-exponential factors for reactions (1) and (2) are 6.1 x 1016 L mol-1 s-1 and 5.5 x 1013 s-1, respectively; the activation energies are 250 and 320 kJ/mol, respectively. Calculate the parts per million of B after 0.5, 1 and 5 seconds. You may assume the heats of reactions (1) and (2) to be constant and equal to -1700 kJ/mol and -800 kJ/mol, respectively. The heat capacities of the gases may be taken to equal that of the inert, 32 J mol−1 K−1, and to be independent of temperature.
4 A + 4 B + C → 4 Y + 6 Z (1)
4 A + 5 C → 4 B + 6 Z (2)
(3)
(4)

## Slide 7: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Write an energy balance design equation for the reactor, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Put the equations in a form suitable for numerical solution
    Does the number of dependent variables equal the number of differential equations?
      If not, eliminate derivatives or add equations until they are equal
    Does each equation have one derivative on the left of the equals sign and a function that does not contain derivatives on the right side of the equals sign
      If not, put the equations in this form,
  Identify the independent variable, the dependent variables, other variable quantities and constants
Provide the items necessary for numerical solution
  the initial values of the independent and dependent variables
  the final value of either the independent variable or one of the dependent variables
  code that evaluates each of the derivatives (i. e. the functions, f, above) given a value for the independent variable and values for each of the dependent variables along with the additional information provided in the problem specification or found in handbooks and reference books

## Slide 8: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them

## Slide 9: Mole Balance Design Equations
4 A + 4 B + C → 4 Y + 6 Z
4 A + 5 C → 4 B + 6 Z

## Slide 10: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Write an energy balance design equation for the reactor, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them

## Slide 11: Energy Balance Design Equation
Expanding the summations
Zero-valued and negligible terms
  Heat input is zero because the reactor operates adiabatically
  Work output is negligible because there are no shafts or moving boundaries (other than, perhaps, an agitator)
  The reactor volume is fixed and the gas fills the entire reactor at all times, so the reaction volume is constant and its derivative is zero
Does the number of dependent variables equal the number of differential equations?
  No, there are 6 equations with 7 dependent variables (the moles of the five reagents, temperature and pressure)
    Eliminate derivatives or add equations until they are equal

## Slide 12: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Write an energy balance design equation for the reactor, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Put the equations in a form suitable for numerical solution
    Does the number of dependent variables equal the number of differential equations?
      If not, eliminate derivatives or add equations until they are equal

## Slide 13
  The derivative of the pressure can be eliminated by use of the ideal gas law
  Recall
  Substitute
  Substitute in the energy balance

## Slide 14: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Write an energy balance design equation for the reactor, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Put the equations in a form suitable for numerical solution
    Does the number of dependent variables equal the number of differential equations?
      If not, eliminate derivatives or add equations until they are equal
    Does each equation have one derivative on the left of the equals sign and a function that does not contain derivatives on the right side of the equals sign
      If not, put the equations in this form,
  Identify the independent variable, the dependent variables, other variable quantities and constants

## Slide 15: Put the Equations in a Form Suitable for Numerical Solution
Does each equation have one derivative on the left of the equals sign and a function that does not contain derivatives on the right side of the equals sign?
  If not, put the equations in this form,
Identify
  the independent variable: t
  the dependent variables: nA, nB, nC, nY, nZ, T
  other variable quantities: r1, r2
  constants: V, ΔH1, ΔH2, nI, Ĉp,I, R

## Slide 16: Step by Step Solution
Formulate the design equations
  Write a mole balance design equation for each reactant and product, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Write an energy balance design equation for the reactor, expanding all summations
    Are there any negligible or zero-valued terms? If so, eliminate them
  Put the equations in a form suitable for numerical solution
    Does the number of dependent variables equal the number of differential equations?
      If not, eliminate derivatives or add equations until they are equal
    Does each equation have one derivative on the left of the equals sign and a function that does not contain derivatives on the right side of the equals sign
      If not, put the equations in this form,
  Identify the independent variable, the dependent variables, other variable quantities and constants
Provide the items necessary for numerical solution
  the initial values of the independent and dependent variables
  the final value of either the independent variable or one of the dependent variables
  code that evaluates each of the derivatives (i. e. the functions, f, above) given a value for the independent variable and values for each of the dependent variables along with the additional information provided in the problem specification or found in handbooks and reference books

## Slide 17: Items Necessary for Numerical Solution
The initial values of the independent and dependent variables
  At the start of the processing step the 3 L reactor contains 1500 ppm of A, 1000 ppm of B and 7% C with the balance being I at 1115 K and 1.7 atm
    t = 0, nY = 0, nZ = 0, T = 1115 K
    also note:
The final value of either the independent variable or one of the dependent variables
  The problem asks us to calculate the parts per million of B after 0.5, 1 and 5 s, so the final value of t is known
Code that evaluates each of the derivatives given a value for the independent variable and values for each of the dependent variables along with the additional information provided in the problem specification or found in handbooks and reference books
  Given: t, nA, nB, nC, nY, nZ, T
  Known constants: V, ΔH1, ΔH2, nI, Ĉp,I, R
  To evaluate the derivatives, use these quantities to calculate r1 and r2
    All quantities in expressions for r1 and r2 are known or given except CA and CB
  Have all values needed to evaluate the derivatives

## Slide 18: Activity 19.2
Many mathematics programs provide code that can solve sets of ODEs written in the form
  M is called the mass matrix
Reformulate the design equations for Activity 19.1 in this form
  Starting with this set of equations
  Add a seventh equation from the ideal gas law
  Write out the mass matrix and the functions, f

## Slide 19: Forming the Mass Matrix
Write the equations with all derivatives on the left of the equals signs and no derivatives on the right
f1 - f7

## Slide 21: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors