## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 20

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Modeling and Optimizing Batch Reactor Operational Protocols
Each step in the operational protocol for a batch reactor is modeled separately
  The mole balances typically are the same for every step
  Each step usually has slightly different energy balance design equations
    Most commonly, the heat input terms are different in each step
As soon as one step ends, the next step begins immediately
  The values of the dependent variables at the end of the prior step become the initial values of the dependent variables for the current step
The net rate of production of a product can be used as a preliminary optimization criterion for the operational protocol
  The net rate of production accounts for both the reaction time and the turnaround time.
If the turnaround time is negligible, short reaction times typically correspond to high net rates, but low product purity
If the turnaround time is comparable to the reaction time, intermediate processing times correspond to high net rates, but product purity is still greater at high processing times

## Slide 4: Questions?

## Slide 5: An Optimization Problem
Consider the batch reactor process described in Example 20.1, and suppose that the maximum permissible temperature of the reacting solution is 90 ºC. Also assume that during the second step of the operational protocol, the coolant flow rate can be programmed to have any value between 0.1 and 1.5 kg min-1 as a function of time. Specify the final temperature for the first step and a coolant flow rate program for the second step with the objective of maximizing the net rate of production of B without exceeding a reaction volume temperature of 90 ºC at any point in the operation and with a minimum conversion of 70%. At the end of the second step in the protocol, the temperature of the reacting fluid must equal 25 ºC.

## Slide 6: Programming the Coolant Flow
The coolant flow rate does not need to be constant
  With the use of a control valve, it could be continually changing
  Alternatively, it could be changed periodically in steps
  High flow rates cause faster cooling
A programmed flow rate must be incorporated into the code you provide to evaluate the ODEs
  Recall, you will be given the current values of the independent and dependent variables
    Thus, you can adjust the coolant flow based on elapsed time (the independent variable) or the reaction volume temperature (a dependent variable)
  To do so
    Use a series of “if” statements
      if T > T1, ṁ = ṁ1
      if T > T2, ṁ = ṁ2
      etc.
    Pick a function to describe the variation in ṁ
      ṁ = a + bt + ct2 + ...

## Slide 7: Optimization Guidelines
The largest possible net rate (not accounting for turnaround time) would be obtained if
  The reactor was instantaneously heated to 90 ºC
  The reaction ran isothermally at 90 ºC to 70% conversion
  The reactor was instantaneously cooled to 25 ºC
The first step is not possible
  Rate of heating is fixed by the coil and the temperature of the steam in it
  Cooling cannot instantaneously stop the temperature rise; the temperature will always continue to rise until the cooling can “kick in”
  Therefore, heat to as high a T as possible in step 1 so that when maximum coolant flow rate is applied, the maximum temperature is 90 ºC
    This will bring the reactor to 90 ºC in as short a time as possible
The second step may be possible
  Once the reactor reaches 90 ºC, program the coolant flow rate over time (decrease it, since the rate of heat generation will be decreasing) to keep the temperature as high as possible (isothermal at 90 ºC, if possible)
  Continue the second step until the conversion is nearly 70% (see next step)
Use the maximum coolant flow during the third step
  This will cool the system as fast as possible
  Choose the final conversion in step 2 so that the added amount of reaction that occurs during the third step just brings the conversion to 70%

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors