## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 20

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Modeling and Optimizing Batch Reactor Operational Protocols
Each step in the operational protocol for a batch reactor is modeled separately
  The mole balances typically are the same for every step
  Each step usually has slightly different energy balance design equations
    Most commonly, the heat input terms are different in each step
As soon as one step ends, the next step begins immediately
  The values of the dependent variables at the end of the prior step become the initial values of the dependent variables for the current step
The net rate of production of a product can be used as a preliminary optimization criterion for the operational protocol
  The net rate of production accounts for both the reaction time and the turnaround time.
If the turnaround time is negligible, short reaction times typically correspond to high net rates, but low product purity
If the turnaround time is comparable to the reaction time, intermediate processing times correspond to high net rates, but product purity is still greater at high processing times

## Slide 4: Questions?

## Slide 5: An Optimization Problem
Consider the batch reactor process described in Example 20.1, and suppose that the maximum permissible temperature of the reacting solution is 90 ºC. Also assume that during the second step of the operational protocol, the coolant flow rate can be programmed to have any value between 0.1 and 1.5 kg min-1 as a function of time. Specify the final temperature for the first step and a coolant flow rate program for the second step with the objective of maximizing the net rate of production of B without exceeding a reaction volume temperature of 90 ºC at any point in the operation and with a minimum conversion of 70%. At the end of the second step in the protocol, the temperature of the reacting fluid must equal 25 ºC.

## Slide 6: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
    18. Reaction Engineering of Batch Reactors
    19. Analysis of Batch Reactors
    20. Optimization of Batch Reactor Processes
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors