## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 21

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
    21. Reaction Engineering of CSTRs
    22. Analysis of Steady State CSTRs
    23. Analysis of Transient CSTRs
    24. Multiple Steady States in CSTRs
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reaction Engineering with CSTRs
Typically CSTRs are designed to operate most of the time at steady state
Transient operation occurs whenever a reactor variable is changed
  Start up and shut down are examples of transient operation
Factors that favor CSTRs
  Liquid phase reaction
  Large quantities of reactant to be processed
  Exothermic reactions
  Reactions with “unusual” kinetics
    Reactant inhibited reactions
    Auto-catalytic reactions
  Cold feed and exothermic reaction (auto-thermal operation)
    Feed is heated due to being mixed directly into the hot reactor contents; no need for a separate heat exchanger
Disadvantages
  For reactions with “typical” kinetics, the rate of reaction is low throughout the process
    Due to mixing, reactant concentration is low and product concentration is high
    Need larger reactor volume (compared to batch or plug flow reactor)
  Not well-suited to gas phase reactions because gases are hard to “stir.”

## Slide 4: Qualitative Analysis of CSTRs
Steady state CSTRs are fundamentally different from batch reactors
  The composition and temperature change during the time that reaction occurs in a batch reactor
    The amount of time reaction occurs is controlled directly
  The composition and temperature are constant during the time that reaction occurs in a steady state CSTR
    The amount of time reaction occurs is controlled by changing the flow rate
    On average, the reaction occurs for a time equal to the space time, τ
Qualitative analysis of CSTR
  Conversion, concentration, temperature and other profiles as a function of space time behave similar to profiles for batch reactors as a function of processing time
  When comparing to batch reactors at processing times equal to the CSTR space time
    Concentrations and temperature change during the time the fluid is reacting in a batch reactor
    Concentrations and temperature are constant during the time the fluid is reacting in a CSTR
      Their values are the final values; i. e. the reactant concentration is low and the product concentration is high
      In an adiabatic reactor, the temperature is the final value; higher for exothermic reactions and lower for endothermic reactions

## Slide 5: Questions?

## Slide 6: Activity 21.1
The handout for Activity 21.1 lists 10 problems, each involving a CSTR
Read through each problem and
  Determine whether it calls for the analysis of a steady state CSTR or a transient CSTR
  If you decide a problem involves a transient analysis, justify your response by identifying at least one reactor variable that will change over time

## Slide 7: Activity 21.1
Question 1: steady state
Question 2: transient
  The outlet cell mass, among other things, will vary over time
Question 3: transient
  The outlet concentrations of all reagents will vary over time
Question 4: steady state
Question 5: steady state
Question 6: transient
  The reactant concentrations leaving the reactor will vary over time
Question 7: steady state
  The outlet concentration of Z will not vary with time
Question 8: steady state
Question 9: transient
  The outlet concentrations of reactants and products will vary over time
Question 10: transient
  The outlet temperature will vary over time

## Slide 8: Qualitative Analysis of a CSTR
Perform a qualitative analysis of a CSTR within which an auto-catalytic reaction is taking place isothermally. Sketch the conversion versus the space time. Then qualitatively compare to the behavior for the same reaction taking place in a perfectly mixed batch reactor.

## Slide 9: Qualitative Analysis
Key Facts
  Reactor is isothermal, therefore no thermal effects
  Reaction is autocatalytic, therefore the rate increases as the concentration of product increases
Qualitative Analysis of CSTR
  Conversion equals zero at space time of zero
  Conversion increases as the space time increases, so initial slope is positive
  Further increase in the space time increases the conversion
    Therefore the product concentration increases
    Therefore the rate increases
    Therefore, the change in the conversion becomes greater
    The plot of conversion versus space time will initially be concave up (increasing slope)
  That trend can’t continue for all space times; the conversion would go to infinity
    Eventually the depletion of reactant causes the rate to decrease with increasing space time
    Therefore, the rate passes through a maximum
    Therefore the conversion passes through an inflection point
  From that point onward, the conversion versus space time slope decreases (concave down)
    As the space time approaches infinity, the slope approaches zero and the conversion approaches its equilibrium value

## Slide 10: Comparison to a Batch Reactor
At low processing times, the rate in the batch reactor will be small because it starts with no product present
At an equal space time, the rate in the CSTR will be larger because for the whole time the fluid reacts, the product is present
Therefore, the CSTR curve will lie above the batch reactor curve
  The batch reactor curve will display an inflection point, just as the CSTR does and for the same reason
    At smaller processing times, the effect of the increasing product concentration predominates and the rate increases
    At larger processing times, the effect of reactant depletion predominates and the rate decreases

## Slide 11: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
    21. Reaction Engineering of CSTRs
    22. Analysis of Steady State CSTRs
    23. Analysis of Transient CSTRs
    24. Multiple Steady States in CSTRs
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors