## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 22

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
    21. Reaction Engineering of CSTRs
    22. Analysis of Steady State CSTRs
    23. Analysis of Transient CSTRs
    24. Multiple Steady States in CSTRs
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: A Generic Approach to the Analysis of a CSTR
Make a schematic diagram
  Incorporate all known specifications, putting them in a consistent set of units
  Introduce any shorthand notation, e. g. A + B → Y + Z
Gather necessary physico-chemical data
Perform an equilibrium analysis
  Verify that rate expressions are accurate at equilibrium
Write the design equations
  One mole balance for each reactant and product of any of the reactions taking place
  An energy balance on the reaction volume
  If needed, an energy balance on the heat transfer fluid
Convert the equations to a single type of composition variable
  Molar flow rates, ṅi
Make sure the equations are properly formulated
  N equations in N unknowns
  Use additional system specifications to eliminate unknowns
  Assume a basis, if appropriate
Solve the design equations (probably numerically) and complete the assigned task or analysis

## Slide 4: Design Equations and Other Useful Relationships
Mole Balance
Energy Balance on the Reacting Fluid
Energy Balance on a Perfectly Mixed Heat Transfer Fluid
Other Relationships
Sensible Heat Term

## Slide 5: Questions?

## Slide 6: Activity 22.1
In Example 20.2, the operation of a batch reactor was analyzed. Specifically, a coolant flow rate of 0.2 kg min-1 was selected to maximize the net rate of production of B (0.0153 mol min-1 including turnaround time) via reaction (1). Suppose that reactor is converted to a CSTR that operates with a space time equal to the total processing time of the two steps in the batch reactor operational protocol (63.8 min). That is, the feed to the CSTR has the same composition and temperature as the initial charge to the batch reactor (a 2 M solution of A at 23 ºC), and the 20 ºC cooling water flows into the jacket at a rate of 0.2 kg min-1. What will the final steady state temperature and outlet molar flow rate of B equal?
The rate expression for reaction (1) is given in equation (2). The heat of reaction (1) may be taken to be constant and equal to -22,200 cal mol-1. The heat capacity of the reacting solution is approximately constant and equal to 440 cal L-1 K-1, and its density is constant. The reaction volume is 4 L, and the jacket volume is 0.5 L with a heat transfer area of 0.6 ft2 and a heat transfer coefficient of 1.13 x 104 cal ft-2 h-1 K-1. The cooling water may be taken to have a constant density of 1 g cm-3 and a constant heat capacity of 1 cal g-1 K-1.
A → B (1)
(2)

## Slide 7: Activity 22.2
Continuing Activity 22.1, find the space time that maximizes the steady state outlet molar flow rate of B from the CSTR.
Using the space time found above, along with all other reactor parameters, as a base case, predict how a small increase in each operating parameter (inlet concentration of A, inlet concentration of B, inlet temperature, volumetric flow rate, coolant flow rate and inlet coolant temperature) will affect the conversion and the outlet flow rate of B. Then perform simulations to confirm or refute your predictions. If your prediction was wrong, make sure you can qualitatively explain the correct outcome.

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
    21. Reaction Engineering of CSTRs
    22. Analysis of Steady State CSTRs
    23. Analysis of Transient CSTRs
    24. Multiple Steady States in CSTRs
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors