## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 25

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: PFR Characteristics
Environmental variables change along length of reactor
Heat transfer area is limited to the reactor wall
Area to Volume is more limited than a CSTR
  Can’t add a coil inside the fluid
Only option for increasing area is to use smaller diameter tube
  Eventually leads to large pressure drop through reactor
Sometimes can break reactor into segments with some form of heating/cooling between them
Heat/Cool
Here

## Slide 4: PFR Advantages & Disadvantages
Distinguishing Features
  No agitation
    Equally well-suited to gases and liquids
    Preferred if a solid catalyst is being used because less abrasion
  Reactant concentration decreases continually and product concentration increases continually from inlet to outlet
  Temperature may vary over the length of the reactor
Preferred Uses
  Reactions that require a solid catalyst
  Large quantities of reactant to be processed
  Reactions that will be run adiabatically or with little heating/cooling
  Reactions with “typical” kinetics
    High rate or selectivity is favored by high reactant concentration and low product concentration
    Same kinds of reactions as are favored in a batch reactor
  Reversible reactions

## Slide 5: Analogy between Batch Reactors and PFRs
Fluid element within a PFR is like a batch reactor
  perfectly mixed radially
  differentially thick so negligible axial differences
  no fluid enters the element or leaves it during process
Starts reacting when fluid element enters the reactor and stops when it leaves
  processing time is equal to the residence time (space time)
Qualitatively, PFR performance as a function of space time is the same as the qualitative performance of a batch reactor as a function of processing time
dz

## Slide 6: Questions?

## Slide 7: Activity 25.1
Suppose reaction (1) and reaction (2) are typical irreversible reactions and further assume that they have exactly the same rate expression (same reaction orders, same pre-exponential factor and same activation energy). In fact, the only difference between them is that reaction (1) is exothermic and reaction (2) is endothermic. Make a single graph showing conversion of A versus space time, and on that graph sketch what the plot would look like (a) for reaction (1) taking place in an adiabatic PFR, (b) for reaction (1) taking place in an isothermal PFR, (c) reaction (2) taking place in an adiabatic PFR and (d) reaction (2) taking place in an isothermal PFR. For each plot explain why it has the shape it does, and then explain why the plots differ from each other in the way they do.
A → B (1)
A → C (2)

## Slide 8: Key Features to Determine
For each curve
  Initial value
  Initial slope
  Initial curvature
    Can it persist?
  Competing effects
    Minimum, maximum or inflection point
  Asymptotic final value
Comparing curves
  Always above, always below or cross at some point

## Slide 9: Activity 25.2
The objectives of this activity are
  Identify two different types of transient responses to a step change in a PFR operating parameter
  Understand what feature of the step change leads to each type of transient response
  Examine the duration of the response of a PFR to a step change in one of its operating parameters
We will use the PFR shown above in a series of thought experiments to qualitatively probe the transient response of a PFR to a set of step changes in operating parameters
  At the instant shown, the step change has just occurred
  The green and blue fluid elements are both inside the reactor
    The green fluid element is the last one to have entered before the step change
    The blue fluid element entered just before the green one
  The red and yellow fluid element are both outside the reactor
    The yellow fluid element will be the first one to enter after the step change
    The red fluid element will enter right after the yellow one

## Slide 10: Duration of the Transient
There was some unspecified step change right after the green fluid element entered the reactor
Will the changes that occur in the red fluid element as it moves through the reactor be exactly the same as the changes that occur in the yellow fluid element as it moves through the reactor?
  Why or why not?
Once the yellow fluid element has reached the outlet from the reactor, will the changes that occur in the next fluid element to enter the reactor as it moves through the reactor be exactly the same as the changes that occur in the yellow fluid element as it moved through the reactor?
  Is there a name for this condition
On the basis of your answers, can you state how long the transient lasted?

## Slide 11: First Step Change
There was a step change in the inlet composition
As the green fluid element moves through the reactor, will it experience the exact same changes that the blue element experiences?
  Why or why not?
As the yellow fluid element moves through the reactor, will it experience the exact same changes that the green fluid element experiences?
  Why or why not?
As the red fluid element moves through the reactor, will it experience the exact same changes that the yellow fluid element experiences?
  Why or why not?
What would change if there was a step change in the inlet temperature

## Slide 12: First Step Change
Based on the answers you gave on the previous slide, describe what changes you would observe as a function of time if you observed at the point indicated

## Slide 13: A Different Kind of Step Change
There was a step change increase in the flow rate
As the green fluid element moves through the reactor, will it experience the exact same changes that the blue element experiences?
  Why or why not?
As the yellow fluid element moves through the reactor, will it experience the exact same changes that the green fluid element experiences?
  Why or why not?
As the red fluid element moves through the reactor, will it experience the exact same changes that the yellow fluid element experiences?
  Why or why not?
Suppose instead of the flow rate, the temperature of the reactor wall changed (causing a step change in the heat transfer term)?

## Slide 14: Second Step Change
Based on the answers you gave on the previous slide, describe what changes you would observe as a function of time if you observed at the point indicated
Compare and contrast the nature of the transient for the preceding case to this case

## Slide 15: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors