## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 26

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: The Steady State PFR Design Equations
Mole balance on i:
Energy balance:
Momentum balance (unpacked tube):
Momentum balance (packed bed):
The unpacked tube momentum balance introduces the volumetric flow rate as an “extra” dependent variable
  Liquids can often be assumed to have constant density, in which case the derivative of the volumetric flow rate with respect to axial position equals zero
  The equation of state can be used for gases
    For an ideal gas: with

## Slide 4: A Problem-Solving Strategy*
Assign the appropriate variable symbol to each quantity that appears in the problem statement and convert them to consistent units
If necessary, assume a basis
Write the design equations in the preferred form with zero-valued terms eliminated and all sums and continuous products fully expanded
  They will form a set of coupled initial value ordinary differential equations
Write equations or values for the things needed to solve initial value ODEs
  Initial values
  One final value
  Every quantity other than the derivatives, the independent and the dependent variables that (a) appears in the anywhere in the ODEs and (b) has not already been assigned a value in preceding steps
Write equations needed, after solving the ODEs, to calculate any other quantities that the problem asks for
*Every problem is different, so be prepared to adapt or modify this approach to suit the particular problem being solved

## Slide 5: Questions?

## Slide 6: Activity 26.1
A gas mixture containing 5% of the reactant A and 20% of the reactant B (balance inert, I) at 350 °C and 2 atm needs to be processed to convert 80% of the A according to irreversible reaction (1). Reaction (1) is first order in A; the pre-exponential factor is 1.4 x 106 min-1 and the activation energy is 30 kcal mol-1. The heat of reaction (1) is constant and equal to −25 kcal mol-1, and the constant pressure molar heat capacity of the gas mixture is approximately equal to 4 times the ideal gas constant. If an adiabatic PFR with negligible pressure drop is used, what space time will be required and what will be the outlet temperature of the gas?
2 A + B → 2 Y + 2 Z (1)

## Slide 7: Defining the Problem
What type of reactor does this problem involve, and how is that reactor operated?
Is this a kinetics problem or a reaction engineering problem?
Write the generic form(s) of the design equation(s) that are needed to construct a model for this reactor

## Slide 8: Defining the Problem
What type of reactor does this problem involve, and how is that reactor operated?
  Steady State PFR operating adiabatically and with negligible pressure drop
Is this a kinetics problem or a reaction engineering problem?
  Reaction engineering: the rate expressions for all reactions are known, the question are related to the operation of the reactor
Write the generic form(s) of the design equation(s) that are needed to construct a model for this reactor
  Steady state PFR mole balance:
  Steady state PFR energy balance:
  Momentum balance is not needed since the reactor is specified to operate with negligible pressure drop

## Slide 9: Identify the Known Quantities
Read through the problem statement and each time a quantity is given, assign that quantity to the appropriate variable
If none of the quantities defined above are extensive, select a basis for your calculations
Optionally, make a schematic diagram of the reactor

## Slide 10: Identify the Known Quantities
Read through the problem statement and each time a quantity is given, assign that quantity to the appropriate variable
  yA0 = 0.05 (5% A in the feed), yB0 = 0.20, yI0 = 0.75, T0 = 350 ºC = 623 K, P0 = 2 atm, fA = 0.8 (80% conversion of A), k0 = 1.4 x 109 min-1, E = 30 kcal mol-1, ΔH1(T) = −25 kcal mol-1 and Ĉp,gas = R = 1.987 x 10-3 kcal mol-1 K-1.
  Since the given inlet mole percentages add to 100%: yY0 = 0 and yZ0 = 0
  Since the pressure drop is negligible: P = P0
If none of the quantities defined above are extensive, select a basis for your calculations
  All quantities listed above are intensive
  As a basis, let ṅ0total = 100 mol min-1
  Having chosen a basis, the following constant quantities can be calculated
    ṅ0i = yY0 ṅ0total (i = A, B, I, Y and Z)
    ṅAf = ṅ0A (1-fA)

## Slide 11: Schematic Diagram
2 A + B → 2 Y + 2 Z

## Slide 12: Construct the Reactor Model
Using the generic form(s) of the design equation(s) written down earlier, write a set of design equations that can be used to model the reactor
What type of equations are these, and what will you need to supply in order to solve them numerically?

## Slide 13: Construct the Reactor Model
Using the generic form(s) of the design equation(s) written down earlier, write a set of design equations that can be used to model the reactor
  Mole balances on every reactant and product
  Energy balance
What type of equations are these, and what will you need to supply in order to solve them numerically?
  Coupled ordinary differential equations, we know the values of the independent and dependent variables at the inlet, so they are initial value ODEs
  To solve numerically we must provide
    Initial values of the independent and dependent variables
    A final value of either the independent or one of the dependent variables
    Code that is given values for the independent and dependent variables and uses them to evaluate the functions f1 through f5 above (where the equations are in the standard form)

## Slide 14
Does the solution of the design equations require you to provide initial and final values? If so, give those values or show how to calculate them from what is given in the problem statement
Does the solution of the design equations require you to provide code? If so, identify what quantities will be given to that code and then show the equations needed in order to write the code

## Slide 15
Does the solution of the design equations require you to provide initial and final values? If so, give those values or show how to calculate them from what is given in the problem statement
  The initial value of z is 0; the corresponding values of the dependent variables (ṅA, ṅB, ṅY, ṅZ and T) are shown on the schematic
  The value of ṅA is known at the outlet (it was calculated from using the specified conversion of A and is shown on the schematic diagram)
Does the solution of the design equations require you to provide code? If so, identify what quantities will be given to that code and then show the equations needed in order to write the code
  Code will be given values of z, ṅA, ṅB, ṅY, ṅZ and T, and must use them to evaluate the functions, f1 through f5, given on the previous slide
  Therefore go through each function and if it hasn’t already been identified as a known constant and it isn’t one of the given values, show how to calculate it

## Slide 16
Does the solution of the design equations require you to provide initial and final values? If so, give those values or show how to calculate them from what is given in the problem statement
  The initial value of z is 0; the corresponding values of the dependent variables (ṅA, ṅB, ṅY, ṅZ and T) are shown on the schematic
  The value of ṅA is known at the outlet (it was calculated from using the specified conversion of A and is shown on the schematic diagram)
Does the solution of the design equations require you to provide code? If so, identify what quantities will be given to that code and then show the equations needed in order to write the code
  Code will be given values of z, ṅA, ṅB, ṅY, ṅZ and T, and must use them to evaluate the functions, f1 through f5, given on the previous slide
  Therefore go through each function and if it hasn’t already been identified as a known constant and it isn’t one of the given values, show how to calculate it
  D appears in the equations and it can’t be calculated
    Even if a different basis was chosen, it couldn’t be calculated
    If it was chosen as the basis, the inlet molar flow rates (initial values) could not be calculated
  Because the reactor is adiabatic and operates with negligible pressure drop, the design equations can be re-written
    Substitute:

## Slide 17
The design equations now take the following form
The initial and final condition are the same except the independent variable is now V
  V = 0 instead of z = 0 at the inlet to the reactor
Code will be given values of V, ṅA, ṅB, ṅY, ṅZ and T, and must use them to evaluate the functions, f1′ through f5′
  Going through the functions we find Ĉp,gas and ΔH10(T) which are known constants whose values have already been specified
  Need to calculate r1 and ṅtotal in order to evaluate the functions
  The reaction is first order in A; units on k0 show the rate expression uses CA, not PA
  The concentration is found by definition using the ideal gas law

## Slide 18: Completing the Requested Tasks
What new quantities will you know after the design equations have been solved numerically?
Does the problem ask for quantities other than those obtained by solving the design equations? If so, show how to calculate them

## Slide 19: Completing the Requested Tasks
What new quantities will you know after the design equations have been solved numerically?
  The values of V, ṅA, ṅB, ṅY, ṅZ and T will be known at the outlet
Does the problem ask for quantities other than those obtained by solving the design equations? If so, show how to calculate them
  The problem asks for T (which was found above) and the space time, which is found by definition
    where V was found above, and the inlet volumetric flow rate was calculated at the time the basis was chosen:
  Note, the volume (and outlet molar flow rates) found by solving the design equations only apply for the chosen basis because they are extensive quantities
    but the space time, which is intensive, will be the same no matter what basis is chosen

## Slide 20: Don’t Memorize Equations Instead, Master the Process
Identify the reactor type and how it is being operated
Determine what type of question is being asked
Assign variables to every number given in the problem statement
  If the given information permits the calculation of other constant quantities, calculate those quantities as well
Determine whether a basis can be chosen; if so, choose one
Optionally make a schematic diagram
For a steady state PFR reaction engineering problem, write out the generic forms of the mole, energy and mechanical energy balances
  Write a mole balance on every species that appears at least once as a reactant or product in the reactions taking place, eliminating zero-valued terms, expanding all summations and continuous products and inserting values of stoichiometric coefficients
  As necessary write an energy balance and a mechanical energy balance, eliminating zero-valued terms, expanding all summations and continuous products, inserting values of stoichiometric coefficients and substituting as necessary for the sensible heat term
Write out the initial values and final value needed to solve the equations
Write out equations needed in order to evaluate the equations
Solve the equations
Use the results to answer the questions posed in the problem

## Slide 21: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors