## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 27

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Transient PFR Design Equations
Mole balance:
Energy balance:
Initial conditions
  Values of the dependent variables (ṅi and T) at all values of z in the instant after the change at t = 0
Boundary conditions
  Value of the dependent variables at one fixed position (usually the inlet) as a function of time since the change
Fronts - a special kind of PFR transient
  The transient is initiated by a step change at the reactor inlet
  The step change is not “felt” by any of the fluid within the reactor
  The front moves through the reactor with a velocity equal to the fluid flow rate
  The concentration and temperature profiles ahead of the front are equal to the steady state profile prior to the step change
  The concentration and temperature profiles behind the front are equal to the steady state profile at the inlet conditions after the change

## Slide 4: Questions?

## Slide 5: Activity 27.1
First order, liquid phase reaction (1) takes place in a steady state PFR. The reactor is cooled by a fluid circulating outside the reactor at 100 ºC. Suppose that suddenly the cooling fluid temperature dropped to 30 ºC while all other operating parameters remained the same. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
A → R (1)

## Slide 6: Activity 27.1
First order, liquid phase reaction (1) takes place in a steady state PFR. The reactor is cooled by a fluid circulating outside the reactor at 100 ºC. Suppose that suddenly the cooling fluid temperature dropped to 30 ºC while all other operating parameters remained the same. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
A → R (1)
Fluid that is already inside the reactor will be affected by this change. As a consequence, that fluid will not follow the steady state profiles of molar flow rates and temperature that existed prior to the change as it continues to flow through the reactor. Therefore, the transient will not take the form of a step change front that propagates from the reactor inlet to the outlet

## Slide 7
Suppose the reactor properties (D, L and U) are known and that the volume specific heat capacity and density ( and ρ) are known and constant. If ṅi,ss(z) and Tss(z) are the known steady state profiles of the molar flow rates and temperature prior to the change, is the constant volumetric flow rate, k0 is the pre-exponential factor and E is the activation energy, write the transient mole and energy balances that are needed to model the transient response to the change assuming that the pressure drop is negligible.

## Slide 8
Suppose the reactor properties (D, L and U) are known and that the volume specific heat capacity and density ( and ρ) are known and constant. If ṅi,ss(z) and Tss(z) are the known steady state profiles of the molar flow rates and temperature prior to the change, is the constant volumetric flow rate, k0 is the pre-exponential factor and E is the activation energy, write the transient mole and energy balances that are needed to model the transient response to the change assuming that the pressure drop is negligible.
General mole balance:
  Noting the volumetric flow rate is constant and the reaction is first order, mole balances on A and R can be written

## Slide 9
General energy balance:
  Noting that in addition, P is constant, the energy balance can be written
    We are analyzing the transient after the change, so Te = 30 ºC

## Slide 10
Write the initial conditions needed to solve the design equations

## Slide 11
Write the initial conditions needed to solve the design equations
  The initial conditions are the known values of the dependent variables just after the change has been made. In this case
    at t = 0, ṅA(z) = ṅA,ss(z)
    at t = 0, ṅR(z) = ṅR,ss(z)
    at t = 0, T(z) = Tss(z)

## Slide 12
Write the initial conditions needed to solve the design equations
  The initial conditions are the known values of the dependent variables just after the change has been made. In this case
    at t = 0, ṅA(z) = ṅA,ss(z)
    at t = 0, ṅR(z) = ṅR,ss(z)
    at t = 0, T(z) = Tss(z)
Write the boundary conditions needed to solve the design equations

## Slide 13
Write the initial conditions needed to solve the design equations
  The initial conditions are the known values of the dependent variables just after the change has been made. In this case
    at t = 0, ṅA(z) = ṅA,ss(z)
    at t = 0, ṅR(z) = ṅR,ss(z)
    at t = 0, T(z) = Tss(z)
Write the boundary conditions needed to solve the design equations
  The boundary conditions are the known values of each dependent variable as a function of time at one location in the reactor. In this case, the inlet molar flow rates and temperature are known (and they are the same as they were before the change)
    at z = 0, ṅA = ṅA,ss(0) for all t
    at z = 0, ṅR = ṅR,ss(0) for all t
    at z = 0, T = Tss(0) for all t
  Note that the boundary conditions could specify that one or more of the dependent variables changes as a known function of t, that is, the boundary conditions do not require constant values
    If this was true, then the transient would last longer than the reactor space time.

## Slide 14: Activity 27.2
Liquid phase reaction (1), with rate expression (2), is taking place adiabatically in a steady state PFR. The reactor volume is 18 ft3 (4 in diameter by 206 ft long), the volumetric flow rate is constant and equal to 0.8 ft3 min-1. The inlet molar flows of A and B are 0.01 and 0.25 lbmol min-1 at a temperature of 600 ºR. The heat of reaction may be taken to be constant and equal to -1.7 x 104 BTU lbmol-1. The heat capacities of A, B and Z are equal to 1000, 180 and 1200 BTU lbmol-1 °R-1, respectively, and they may be considered to be independent of temperature. Suppose the feed temperature is suddenly changed to 700 ºR. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
A + B ⇄ Z (1)
(2)

## Slide 15: Activity 27.2
Liquid phase reaction (1), with rate expression (2), is taking place adiabatically in a steady state PFR. The reactor volume is 18 ft3 (4 in diameter by 206 ft long), the volumetric flow rate is constant and equal to 0.8 ft3 min-1. The inlet molar flows of A and B are 0.01 and 0.25 lbmol min-1 at a temperature of 600 ºR. The heat of reaction may be taken to be constant and equal to -1.7 x 104 BTU lbmol-1. The heat capacities of A, B and Z are equal to 1000, 180 and 1200 BTU lbmol-1 °R-1, respectively, and they may be considered to be independent of temperature. Suppose the feed temperature is suddenly changed to 700 ºR. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
Fluid that is already inside the reactor when the change occurs will not be affected by the change. It will continue to flow at the same rate and it will continue to react adiabatically. In other words, it will proceed the rest of the way through the reactor as if the reactor was still operating at steady state. The transient will take the form of a step change front that propagates from the reactor inlet to the outlet.

## Slide 16: Activity 27.2
Liquid phase reaction (1), with rate expression (2), is taking place adiabatically in a steady state PFR. The reactor volume is 18 ft3 (4 in diameter by 206 ft long), the volumetric flow rate is constant and equal to 0.8 ft3 min-1. The inlet molar flows of A and B are 0.01 and 0.25 lbmol min-1 at a temperature of 600 ºR. The heat of reaction may be taken to be constant and equal to -1.7 x 104 BTU lbmol-1. The heat capacities of A, B and Z are equal to 1000, 180 and 1200 BTU lbmol-1 °R-1, respectively, and they may be considered to be independent of temperature. Suppose the feed temperature is suddenly changed to 700 ºR. Plot the temperature as a function of z, 11 minutes after the change.
A + B ⇄ Z (1)
(2)

## Slide 17: Position of the Front
A step change front will propagate through the reactor at a constant velocity equal to the volumetric flow rate divided by the cross-sectional area
  The time required for the front to reach the reactor outlet will equal the space time
Ahead of the front, the concentration/temperature profile will remain exactly as it was before the change
Behind the front, the concentration/temperature profile will be exactly equal to the steady state profile for the feed conditions after the step change
When will the front break through?

## Slide 18: Position of the Front
A step change front will propagate through the reactor at a constant velocity equal to the volumetric flow rate divided by the cross-sectional area
  The time required for the front to reach the reactor outlet will equal the space time
Ahead of the front, the concentration/temperature profile will remain exactly as it was before the change
Behind the front, the concentration/temperature profile will be exactly equal to the steady state profile for the feed conditions after the step change
When will the front break through?
  It will take one space time, here
    The front will not have broken through
Where will the front be located (i. e. at what value of z)?

## Slide 19: Position of the Front
A step change front will propagate through the reactor at a constant velocity equal to the volumetric flow rate divided by the cross-sectional area
  The time required for the front to reach the reactor outlet will equal the space time
Ahead of the front, the concentration/temperature profile will remain exactly as it was before the change
Behind the front, the concentration/temperature profile will be exactly equal to the steady state profile for the feed conditions after the step change
When will the front break through?
  It will take one space time, here
    The front will not have broken through
Where will the front be located (i. e. at what value of z)?
  The front travels at the same constant velocity as the fluid:
  After 11 minutes at this velocity, the front will have moved to z = 11 v

## Slide 20: To Generate the Requested Plot
Plot the steady state temperature profile corresponding to the feed temperature after the change from z = 0 to the position of the front
Plot the steady state temperature profile that existed prior to the change from the position of the front to z = L
To calculate each steady state profile
  Write the steady state mole and energy balances
  Identify the independent and dependent variables
  Specify initial conditions for the independent and dependent variables
  Specify the final value of either the independent variable or one of the dependent variables
  Provide code that is given the values of the independent and dependent variables and uses that input to evaluate each of the design equations, when written in the standard form

## Slide 21: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors