## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 27

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Transient PFR Design Equations
Mole balance:
Energy balance:
Initial conditions
  Values of the dependent variables (ṅi and T) at all values of z in the instant after the change at t = 0
Boundary conditions
  Value of the dependent variables at one fixed position (usually the inlet) as a function of time since the change
Fronts - a special kind of PFR transient
  The transient is initiated by a step change at the reactor inlet
  The step change is not “felt” by any of the fluid within the reactor
  The front moves through the reactor with a velocity equal to the fluid flow rate
  The concentration and temperature profiles ahead of the front are equal to the steady state profile prior to the step change
  The concentration and temperature profiles behind the front are equal to the steady state profile at the inlet conditions after the change

## Slide 4: Questions?

## Slide 5: Activity 27.1
First order, liquid phase reaction (1) takes place in a steady state PFR. The reactor is cooled by a fluid circulating outside the reactor at 100 ºC. Suppose that suddenly the cooling fluid temperature dropped to 30 ºC while all other operating parameters remained the same. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
A → R (1)

## Slide 6
Suppose the reactor properties (D, L and U) are known and that the volume specific heat capacity and density ( and ρ) are known and constant. If ṅi,ss(z) and Tss(z) are the known steady state profiles of the molar flow rates and temperature prior to the change, is the constant volumetric flow rate, k0 is the pre-exponential factor and E is the activation energy, write the transient mole and energy balances that are needed to model the transient response to the change assuming that the pressure drop is negligible.

## Slide 7
Write the initial conditions needed to solve the design equations
Write the boundary conditions needed to solve the design equations

## Slide 8: Activity 27.2
Liquid phase reaction (1), with rate expression (2), is taking place adiabatically in a steady state PFR. The reactor volume is 18 ft3 (4 in diameter by 206 ft long), the volumetric flow rate is constant and equal to 0.8 ft3 min-1. The inlet molar flows of A and B are 0.01 and 0.25 lbmol min-1 at a temperature of 600 ºR. The heat of reaction may be taken to be constant and equal to -1.7 x 104 BTU lbmol-1. The heat capacities of A, B and Z are equal to 1000, 180 and 1200 BTU lbmol-1 °R-1, respectively, and they may be considered to be independent of temperature. Suppose the feed temperature is suddenly changed to 700 ºR. Would the transient take the form of a step change front that propagates from the reactor inlet to the outlet?
A + B ⇄ Z (1)
(2)

## Slide 9: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors