## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 28

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Choosing the Type of Reactor to Use
Safety: are any of the ideal reactor types inherently risky with respect to safe operation?
Practicality: can any of the ideal reactor types be eliminated from consideration for practical reasons?
Existing technology: is this reaction system, or one that is chemically similar, already being operated commercially?
Batch versus Continuous
  Batch processing is more labor intensive and costly than continuous
  Best for chemicals where the total amount to be produced is small and the price of the product is high
Continuous processing
  Best when the amount to be processed is large
CSTR versus PFR
  In a CSTR, the reaction only takes place at the final conditions
    low reactant, high product and final temperature
  In a PFR, the reaction starts at the inlet conditions and occurs at continually changing conditions, only reaching the CSTR conditions at the end of processing
    initially high reactant, low product and feed temperature
Qualitative analysis won’t always provide a clear best choice
  Perform quantitative analysis of each of the possible choices

## Slide 4: Questions?

## Slide 5: Activity 28.1
Irreversible, liquid phase reaction (1) is first order in A with a pre-exponential factor equal to 1 x 108 min-1 and an activation energy of 50 kJ mol-1. It takes place in the solution phase where the density is constant. The reaction is exothermic with a constant heat of reaction equal to -180 kJ mol-1; the solution heat capacity is also constant and equal to 3.95 kJ L-1 K-1. A reactor is needed to process 300,000 L day-1 of a 298 K solution containing A at a concentration of 1 M. For conversions in the range from 20% to 90%, what reactor would you recommend?
A → Z (1)

## Slide 6: Activity 28.1
Irreversible, liquid phase reaction (1) is first order in A with a pre-exponential factor equal to 1 x 108 min-1 and an activation energy of 50 kJ mol-1. It takes place in the solution phase where the density is constant. The reaction is exothermic with a constant heat of reaction equal to -180 kJ mol-1; the solution heat capacity is also constant and equal to 3.95 kJ L-1 K-1. A reactor is needed to process 300,000 L day-1 of a 298 K solution containing A at a concentration of 1 M. For conversions in the range from 20% to 90%, what reactor would you recommend?
A → Z (1)
The Informational Reading suggests that a good way to start a problem of this kind is by performing a qualitative analysis.
  We don’t have cost data, so we’ll assume that small reactor volume and minimal external heating/cooling will minimize investment and operating costs
  Adiabatic operation eliminates external heating/cooling, so let’s first qualitatively analyze how the rate will vary with reaction time (i. e. batch processing time or flow reactor space time)

## Slide 7: Qualitative Analysis
Irreversible, liquid phase reaction (1) is first order in A with a pre-exponential factor equal to 1 x 108 min-1 and an activation energy of 50 kJ mol-1. It takes place in the solution phase where the density is constant. The reaction is exothermic with a constant heat of reaction equal to -180 kJ mol-1; the solution heat capacity is also constant and equal to 3.95 kJ L-1 K-1. A reactor is needed to process 300,000 L day-1 of a 298 K solution containing A at a concentration of 1 M. For conversions in the range from 20% to 90%, what reactor would you recommend?
A → Z (1)
Qualitative rate behavior
  Increase initially due to increasing temperature
  As processing continues, it will reach a maximum and then continuously decrease due to depletion of the reactants
Qualitative flow reactor analysis

## Slide 8: Qualitative Reactor Comparison
Up to the conversion/space time where the rate in a CSTR reaches a maximum
  The rate is the same everywhere in the CSTR and it is greater than the rate anywhere (except the outlet) in the PFR
  If the rate (moles converted per volume) in the CSTR is greater, then the required volume (for a given conversion) is smaller
  CSTR is preferred
Well beyond the conversion/space time where the rate in a CSTR reaches a maximum
  The rate is the same everywhere in the CSTR and it is smaller than than the rate anywhere (except the outlet) in the PFR
  If the rate (moles converted per volume) in the CSTR is smaller, then the required volume (for a given conversion) is larger
  PFR is preferred
At intermediate conversion/ space time, but beyond that where the rate in a CSTR reaches a maximum
  A quantitative analysis is needed in order to determine which reactor is smaller
But before undertaking the quantitative analysis
  Is adiabatic PFR operation feasible?
  Is batch operation feasible?

## Slide 9: Order of Magnitude Analysis
Rate of reaction at the PFR inlet
  this is 17% of the original A per minute, and certainly is large enough for adiabatic operation
Time per batch at the initial rate
  for 20% conversion slightly over 1 minute
  for 90% conversion, approximately 5 and ¼ minutes
  batch reaction times this short may not be practical
    batch to batch consistency may be difficult to maintain
    turnaround time will likely be much longer than reaction time suggesting high labor costs
  using a batch reactor may be feasible, but should not be recommended

## Slide 10: Order of Magnitude Analysis
Rate of reaction at the PFR inlet
  this is 17% of the original A per minute, and certainly is large enough for adiabatic operation
Time per batch at the initial rate
  for 20% conversion slightly over 1 minute
  for 90% conversion, approximately 5 and ¼ minutes
  batch reaction times this short may not be practical
    batch to batch consistency may be difficult to maintain
    turnaround time will likely be much longer than reaction time suggesting high labor costs
  using a batch reactor may be feasible, but should not be recommended
To identify when a PFR is recommended and when a CSTR is recommended a quantitative analysis of each will be needed
  Calculate and plot the reactor volume versus conversion for each reactor
  Determine the conversion where the two lines cross
    On the basis of the qualitative analysis, at smaller conversions, the CSTR line is expected to lie below the PFR line
      a CSTR should be recommended
    At larger conversions, the PFR line is expected to lie below the CSTR line
      a PFR should be recommended

## Slide 11: Quantitative Analysis
Read through the problem and assign correct variable symbol to each quantity given
For the reactor type being analyzed
  Write mole balances on A and Z and an energy balance (ignore PFR pressure drop)
    Eliminate zero-valued terms, expand all summations and continuous products
  Identify, as appropriate, unknowns, independent variables and dependent variables
  Determine the type of equations to be solved and what you will need to provide in order to solve them numerically
    Calculate (or list) any values that will be needed
    Write any additional equations that will be needed
Solve the equations numerically
Use the solution to plot reactor volume versus conversion, per the preceding slide
Repeat for the other reactor and determine the conversion where the plots cross
  Check that the results agree with the qualitative analysis

## Slide 12
Known constants: k0 = 1 x 108 min-1, E = 50 kJ mol-1, ΔH = -180 kJ mol-1, Cp = 3.95 kJ L-1 K-1, T0 = 298 K, CA0 = 1 mol L-1, fA = 0.2 to 0.9, ṅZ0 = 0 and 300,000 L day-1
Universal and calculated constants: R = 8.3145 J mol-1 K-1 and
Mole and energy balances
  To solve numerically you need
Non-linear algebraic equations
Initial value ODEs
Unknowns: V, ṅZ and T
Independent: V; Dependent: ṅA, ṅZ and T
Code to evaluate the equations
above, given the unknowns
Initial values: V = 0, ṅA = ṅA0, ṅZ = ṅZ0, T = T0
Final value: ṅA = ṅA0(1 - fA)
Code to evaluate derivatives above, given
independent and dependent variables
To solve numerically you need

## Slide 13: Volume vs. Conversion

## Slide 14: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors