## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 28

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Choosing the Type of Reactor to Use
Safety: are any of the ideal reactor types inherently risky with respect to safe operation?
Practicality: can any of the ideal reactor types be eliminated from consideration for practical reasons?
Existing technology: is this reaction system, or one that is chemically similar, already being operated commercially?
Batch versus Continuous
  Batch processing is more labor intensive and costly than continuous
  Best for chemicals where the total amount to be produced is small and the price of the product is high
Continuous processing
  Best when the amount to be processed is large
CSTR versus PFR
  In a CSTR, the reaction only takes place at the final conditions
    low reactant, high product and final temperature
  In a PFR, the reaction starts at the inlet conditions and occurs at continually changing conditions, only reaching the CSTR conditions at the end of processing
    initially high reactant, low product and feed temperature
Qualitative analysis won’t always provide a clear best choice
  Perform quantitative analysis of each of the possible choices

## Slide 4: Questions?

## Slide 5: Activity 28.1
Irreversible, liquid phase reaction (1) is first order in A with a pre-exponential factor equal to 1 x 108 min-1 and an activation energy of 50 kJ mol-1. It takes place in the solution phase where the density is constant. The reaction is exothermic with a constant heat of reaction equal to -180 kJ mol-1; the solution heat capacity is also constant and equal to 3.95 kJ L-1 K-1. A reactor is needed to process 300,000 L day-1 of a 298 K solution containing A at a concentration of 1 M. For conversions in the range from 20% to 90%, what reactor would you recommend?
A → Z (1)

## Slide 6: Activity 28.1
Irreversible, liquid phase reaction (1) is first order in A with a pre-exponential factor equal to 1 x 108 min-1 and an activation energy of 50 kJ mol-1. It takes place in the solution phase where the density is constant. The reaction is exothermic with a constant heat of reaction equal to -180 kJ mol-1; the solution heat capacity is also constant and equal to 3.95 kJ L-1 K-1. A reactor is needed to process 300,000 L day-1 of a 298 K solution containing A at a concentration of 1 M. For conversions in the range from 20% to 90%, what reactor would you recommend?
A → Z (1)
The Informational Reading suggests that a good way to start a problem of this kind is by performing a qualitative analysis.
  We don’t have cost data, so we’ll assume that small reactor volume and minimal external heating/cooling will minimize investment and operating costs
  Adiabatic operation eliminates external heating/cooling, so let’s first qualitatively analyze how the rate will vary with reaction time (i. e. batch processing time or flow reactor space time)

## Slide 7: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors