## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 29

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reactor Networks
Reasons for using multiple reactors
  Add capacity to an existing process
  Performance Advantages
    Heat management
    More favorable composition vs. space time
No difference in model for an individual reactor
  Equations may become coupled with those for another reactor
  May need additional mole and energy balances at splitting and mixing points
General behavior
  Two PFRs (of equal diameter) connected in series are equivalent to a single PFR with their combined length provided no heating, cooling or fluid exchange takes place between them
  Mixing two streams of unequal conversion generally decreases the performance of a parallel reactor network compared to networks where such mixing does not occur
CSTR cascades (CSTRs in series)
  As the number of CSTRs in the cascade increases, keeping total volume constant, the cascade performs more and more like a PFR
Series
Parallel

## Slide 4: Advantage of a CSTR Cascade over a Single CSTR
Outlet composition
and temperatures
are equal
Inlet composition
and temperatures
are equal
Rates are
Equal
Rate is
Higher
Since some of the reaction occurs
at a higher rate with 2 reactors
the total volume is smaller

## Slide 5: Questions?

## Slide 6: Activity 29
Consider the irreversible, liquid phase reaction A → B which occurs at constant density. Reactant A is supplied at a rate of 4 L min-1 in a concentration of 2 mol L-1 and at a temperature of 43 ºC. The heat capacity of the fluid is 0.87 cal mL-1 K-1 and the heat of reaction is -27.2 kcal mol-1. The reaction is second order in the concentration of A, and the rate coefficient obeys Arrhenius’ law with a pre-exponential factor of 6.37 x 109 L mol-1 min-1 and an activation energy of 14.3 kcal mol-1. It is desired to convert 90% of the reactant to product adiabatically. Consider the following reactor networks: (a) a single CSTR, (b) a single PFR, (c) two CSTRs in series, (d) a CSTR followed in series by a PFR, and (e) a PFR followed in series by a CSTR. Determine which reactor network requires the smallest total reactor volume. (In each of the reactor networks, the two reactors are not required to have equal volumes.)

## Slide 7: Activity 29
Consider the irreversible, liquid phase reaction A → B which occurs at constant density. Reactant A is supplied at a rate of 4 L min-1 in a concentration of 2 mol L-1 and at a temperature of 43 ºC. The heat capacity of the fluid is 0.87 cal mL-1 K-1 and the heat of reaction is -27.2 kcal mol-1. The reaction is second order in the concentration of A, and the rate coefficient obeys Arrhenius’ law with a pre-exponential factor of 6.37 x 109 L mol-1 min-1 and an activation energy of 14.3 kcal mol-1. It is desired to convert 90% of the reactant to product adiabatically. Consider the following reactor networks: (a) a single CSTR, (b) a single PFR, (c) two CSTRs in series, (d) a CSTR followed in series by a PFR, and (e) a PFR followed in series by a CSTR. Determine which reactor network requires the smallest total reactor volume. (In each of the reactor networks, the two reactors are not required to have equal volumes.)
Start with a qualitative analysis
  How will the rate change as the space time increases?
  Which of the reactors or reactor networks is better suited to the rate versus conversion profile
    When the rate is larger, the required volume is smaller

## Slide 8: Qualitative Analysis
The reaction is exothermic and irreversible
  As conversion increases, the rate will increase, pass through a maximum and then decrease
You can’t say for sure which reactor or network is preferred because you don’t know what conversion corresponds to the maximum rate
  If the maximum rate occurs near 90% conversion, a single CSTR would probably be best because throughout the reactor, the rate would be high, leading to a smaller volume
  If the maximum rate occurs at conversions well below 90%, a CSTR sized to operate at near the maximum rate followed by a PFR would probably be best
Note, a PFR always operates right on the rate versus space time (or conversion) curve
  In a conversion range where the rate is continually increasing, a CSTR will be smaller
  In a conversion range where the rate is continually decreasing, a PFR will be smaller
Now proceed to the quantitative analysis of the five cases
  Write design equations for each reactor in the network
  Identify each flow stream (a, b, c, etc.) and determine whether the molar flows and the temperature are known
  Solve the design equations to find the reactor volume or volumes
    When there are two reactors, pick the volume of the first reactor, solve the equations for the total volume and repeat
    Plot the total volume versus the volume of the first reactor to find the minimum

## Slide 9: Design Equations
Write design equations that can be used to analyze any of the CSTRs

## Slide 10: Design Equations
Write design equations that can be used to analyze any of the CSTRs
  3 equations, so 3 unknowns
    ṅB,out and Tout in all cases
    ṅA,out when CSTR is the first reactor
    V when CSTR is the second reactor
Write design equations that can be used to analyze any of the PFRs
  Final condition
    V when PFR is the first reactor
    ṅA,out when PFR is the second reactor

## Slide 11: Individual Reactors
For every CSTR
  Design equations from previous slide
  ṅB,out and Tout are unknown
For first CSTR if there are 2 reactors
  ṅA,out is unknown
For last CSTR
  V is unknown
For every PFR
  Design equations and initial conditions from previous slide
For first PFR if there are 2 reactors
  Final value is V
For last PFR
  Final value is ṅA,out

## Slide 12: Numerical Solution
For the single reactors, simply solve the design equations to find V
For each reactor network
  Pick a range of values for the first reactor volume between zero and the volume of the single reactor found above
  For each volume in that range
    Solve the design equations for the first reactor to get molar flow rates of A and B and temperature for stream b in diagrams
    Use those results to solve the design equations for the second reactor to get its volume
    Calculate the total volume and plot it versus the volume of the first reactor
  Find the minimum in the plot and from it, read the minimum volume for that reactor network
Solving the CSTR design equations requires a guess for the solution
  It may be difficult or impossible to find a single guess that works over the whole range of volumes
    Either solve over smaller ranges of volume
    Or write the code so the guesses are varied appropriately

## Slide 13: Numerical Solution
For the single reactors, simply solve the design equations to find V
For each reactor network
  Pick a range of values for the first reactor volume between zero and the volume of the single reactor found above
  For each volume in that range
    Solve the design equations for the first reactor to get molar flow rates of A and B and temperature for stream b in diagrams
    Use those results to solve the design equations for the second reactor to get its volume
    Calculate the total volume and plot it versus the volume of the first reactor
  Find the minimum in the plot and from it, read the minimum volume for that reactor network
Solving the CSTR design equations requires a guess for the solution
  It may be difficult or impossible to find a single guess that works over the whole range of volumes
    Either solve over smaller ranges of volume
    Or write the code so the guesses are varied appropriately
Results from smallest to largest
  Single CSTR (7.0 L) > 2 CSTRs (2.7 L) > single PFR = PFR before CSTR (1.7 L) > CSTR before PFR (1.5 L)

## Slide 14: Volume Plots

## Slide 15: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors