## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 29

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Reactor Networks
Reasons for using multiple reactors
  Add capacity to an existing process
  Performance Advantages
    Heat management
    More favorable composition vs. space time
No difference in model for an individual reactor
  Equations may become coupled with those for another reactor
  May need additional mole and energy balances at splitting and mixing points
General behavior
  Two PFRs (of equal diameter) connected in series are equivalent to a single PFR with their combined length provided no heating, cooling or fluid exchange takes place between them
  Mixing two streams of unequal conversion generally decreases the performance of a parallel reactor network compared to networks where such mixing does not occur
CSTR cascades (CSTRs in series)
  As the number of CSTRs in the cascade increases, keeping total volume constant, the cascade performs more and more like a PFR
Series
Parallel

## Slide 4: Advantage of a CSTR Cascade over a Single CSTR
Outlet composition
and temperatures
are equal
Inlet composition
and temperatures
are equal
Rates are
Equal
Rate is
Higher
Since some of the reaction occurs
at a higher rate with 2 reactors
the total volume is smaller

## Slide 5: Questions?

## Slide 6: Activity 29
Consider the irreversible, liquid phase reaction A → B which occurs at constant density. Reactant A is supplied at a rate of 4 L min-1 in a concentration of 2 mol L-1 and at a temperature of 43 ºC. The heat capacity of the fluid is 0.87 cal mL-1 K-1 and the heat of reaction is -27.2 kcal mol-1. The reaction is second order in the concentration of A, and the rate coefficient obeys Arrhenius’ law with a pre-exponential factor of 6.37 x 109 L mol-1 min-1 and an activation energy of 14.3 kcal mol-1. It is desired to convert 90% of the reactant to product adiabatically. Consider the following reactor networks: (a) a single CSTR, (b) a single PFR, (c) two CSTRs in series, (d) a CSTR followed in series by a PFR, and (e) a PFR followed in series by a CSTR. Determine which reactor network requires the smallest total reactor volume. (In each of the reactor networks, the two reactors are not required to have equal volumes.)

## Slide 7: Design Equations
Write design equations that can be used to analyze any of the CSTRs
Write design equations that can be used to analyze any of the PFRs

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors