## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 30

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Thermal Back-Mixing of a PFR
The PFR design equations are the same as a stand-alone PFR
  Often you can’t solve them independently because the inlet temperature, Tb, is not specified
Design equations for the heat exchanger
  Energy balance
  Heat transfer equation (one of the following)

## Slide 4: Analysis of an Integrated Heat Exchanger and PFR
Make a simple schematic and label each of the streams
Assign each quantity that is specified in the problem statement to the appropriate variable
Set up the design equations for the PFR
  If there is sufficient information to solve the PFR design equations
    Solve the PFR design equations
    Use the results to solve the heat exchanger design equations
  If the PFR design equations cannot be solved independently
    Set up the two design equations for the heat exchanger
    In preparation for solving the heat exchanger design equations numerically, choose Tb as one of the unknowns and do not choose Tc or any molar flow rate as the other unknown
    Solve the heat exchanger design equations numerically
      The code you must provide will be given Tb
        knowing that, you can solve the PFR design equations to obtain Tc and any unknown molar flow rates
        knowing those, you can evaluate the heat exchanger design equations
    Once the heat exchanger design equations are solved, use the results to solve the PFR design equations
Answer the questions posed in the problem statement

## Slide 5: Questions?

## Slide 6
An acid, A, is to be hydrolyzed according to the reaction A + W → P, where W represents water and P, the product. The acid will be fed to an adiabatic, steady state PFR at 0.07 kmol/s and water will be fed at 1.67 kmol/s. This gives a total feed flow of 0.04 m3/s. The feed temperature is 300 K. The fluid volume of the PFR is 0.5 m3. The rate expression is given in equation (1), with the rate coefficient given in equation (2) and the equilibrium constant in equation (3). The heat of reaction is -86,000 kJ/kmole at 298 K. The heat capacities of A, W, and P are 412, 76, and 512 kJ/(kmol K), respectively, and may be taken to be independent of temperature. Compare the conversions and final temperatures when (a) the feed enters the PFR directly and (b) when the product stream is used to heat the feed (assume a 5 K cold approach).
(1)
(2)
(3)

## Slide 7: Activity 30.1
In this activity you will practice the general approach for analyzing an integrated heat exchanger and PFR.
It also illustrates a problem where the cold approach is specified and used as one of the heat exchanger design equations instead of the heat transfer equation
Perform all work for this activity on the worksheet that has been provided

## Slide 8: Sketch of the System
Make a sketch of the system, labeling each flow stream.

## Slide 9: Identify Known Quantities
Read through the problem statement. Each time you encounter a quantity, write it down and equate it to the appropriate variable. When you have completed doing so, if there are any additional constant quantities that you know will be needed and that can be calculated from the values you found, write the equations needed for doing so.

## Slide 10: PFR Design Equations
Generate the design equations needed to model the PFR by simplification of the general PFR design equations found in Unit 17 or on the AFCoKaRE Exam Handout.

## Slide 11: Numerical Solution of the PFR Design Equations
Identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations.
Assuming that the PFR design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values.

## Slide 12: Heat Exchanger Design Equations
Set up the heat exchanger design equations (energy balance and either heat transfer equation or specified approach).

## Slide 13: Numerical Solution of the Heat Exchanger Design Equations
Identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations.
Assuming that the heat exchanger design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values.

## Slide 14: Solution
Solve the design equations and use the results to answer the questions asked.

## Slide 15: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors