## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 31

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: A Recycle PFR
The recycle stream, r, mixes a fraction of the product stream with the fresh feed
The PFR design equations are formulated exactly the same as a stand-alone PFR, but often they cannot be solved independently
  In those cases, solve them simultaneous with mole and energy balances on the mixing point, 1
  Define the recycle ratio as the recycle flow, r, divided by the process outlet flow, d
      As the recycle ratio increases from zero, the reactor becomes less like a PFR and more like a CSTR
  Mixing point balances:
Caveats
  Conversion can be defined overall (a to d) or per pass (b to c)
  Concentrations in the PFR are molar flow rates divided by volumetric flow rate in the reactor
    The flow rate in the reactor is greater than the process feed flow rate
  Back-mixing introduces the possibility of multiple steady states

## Slide 4: Analysis of a Recycle PFR
Make a simple schematic and label each of the streams
Assign each quantity that is specified in the problem statement to the appropriate variable
Set up the design equations for the PFR
  If there is sufficient information to solve the PFR design equations
    Solve the PFR design equations
    Use the results to solve the mixing point design equations
  If the PFR design equations cannot be solved independently
    Set up the design equations for the mixing point
    In preparation for solving the mixing point design equations numerically, choose unknowns to be molar flows and temperature of stream b and do not choose them as stream c
    Solve the mixing point design equations numerically
      The code you must provide will be given the molar flows and temperature of stream b
      knowing those you can solve the PFR design equations to obtain the molar flows and temperature of stream c
        knowing those, you can evaluate the mixing point design equations
    Once the mixing point design equations are solved, use the results to solve the PFR design equations
Answer the questions posed in the problem statement

## Slide 5: Questions?

## Slide 6
In liquid phase reaction (1) the chiral molecule, B, is produced autocatalytically according to the rate expression given in equation (2). The heat of reaction is -14 kcal mol-1, independent of temperature. The pre-exponential factor is equal to 4.2 x 1015 cm3 mol-1 min-1 and the activation energy is 18 kcal mol-1. A solvent is used, and the heat capacity of the reacting solution can be taken to equal that of the solvent, 1.3 cal cm-3 K-1. The density of the liquid may be assumed to be constant. The concentrations of A and B in the feed to the process are 2 M and 0 M, respectively, and the flow rate is 500 cm3 min-1 at 300K. An adiabatic recycle PFR with a recycle ratio of 1.3 is used. The reactor diameter is 5 cm and it is 50 cm long. What are the outlet concentrations of A and B and the outlet temperature from the process?
A + B → 2 B (1)
(2)

## Slide 7: Activity 31.1
In this activity you will practice the general approach for analyzing a recycle PFR
Perform all work for this activity on the worksheet that has been provided
Make a sketch of the system, labeling each flow stream

## Slide 8: Identify Known Quantities
Read through the problem statement. Each time you encounter a quantity, write it down and equate it to the appropriate variable. When you have completed doing so, if there are any additional constant quantities that you know will be needed and that can be calculated from the values you found, write the equations needed for doing so.

## Slide 9: PFR Design Equations
Generate the design equations needed to model the PFR by simplification of the general PFR design equations found in Unit 17 or on the AFCoKaRE Exam Handout.

## Slide 10: Numerical Solution of the PFR Design Equations
Identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations.
Assuming that the PFR design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values.

## Slide 11: Mixing Point Balance Equations
Write mole and energy balances for the mixing point

## Slide 12: Numerical Solution of the Mixing Point Design Equations
Identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations.
Assuming that the mixing point design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values.

## Slide 13: Solution
Solve the design equations and use the results to answer the questions asked.

## Slide 14: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
    25. Reaction Engineering of PFRs
    26. Analysis of Steady State PFRs
    27. Analysis of Transient PFRs
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors