## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 32

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
  A. Ideal Reactors
  B. Perfectly Mixed Batch Reactors
  C. Continuous Flow Stirred Tank Reactors
  D. Plug Flow Reactors
  E. Matching Reactors to Reactions
    28. Choosing a Reactor Type
    29. Multiple Reactor Networks
    30. Thermal Back-Mixing in a PFR
    31. Back-Mixing in a PFR via Recycle
    32. Ideal Semi-Batch Reactors
Part IV - Non-Ideal Reactions and Reactors

## Slide 3: Semi-Batch (Semi-Flow) Reactor
A batch reactor where some reactant flows in or some product flows out while the batch is processing
  Neutralization of an acid with a base
    Add base slowly to batch of acid in order to control the rate at which heat is released
  Reversible esterification
    Allow one product to boil off allowing the reaction to reach higher conversion than in a closed batch process
If species are boiling off, the composition of the leaving vapor is related to the composition of the liquid, e. g. by Raoult’s law or Henry’s law
Unlike common batch reactors, often the fluid volume is not constant
  Use the appropriate equation of state to re-write the derivatives of fluid volume and pressure in terms of the moles in the reactor and the temperature

## Slide 4: Semi-Batch Design Equations
Mole balance
  ṅi is the net molar rate of flow of species i into the reactor
      may be a function of time
Energy balance
  is the energy used in heating the incoming stream to the reactor temperature and doing the P-V work associated with flowing in
  Usually,

## Slide 5: Questions?

## Slide 6
The reaction between A and B produces the desired product, D according to reaction (1), but B also decomposes according to reaction (2), generating the undesired product U. The reactions take place in solution, and the heat of reaction is so small that the reactions are effectively isothermal. Reaction (1) is first order in each of the two reactants, second order overall. Reaction (2) is second order in B. At the process temperature the rate coefficient for reaction (1) is 8 x 10-3 L mol-1 min-1 and that for reaction (2) is 4 x 10-3 L mol-1 min-1. A 2000 L stirred tank reactor will be used, taking its feed from one solution containing A at a concentration of 3 mol L-1 and from a second containing B at a concentration of 1 mol L-1. Compare the selectivity (mol D per mol U) that will result from a batch process charged with 500 L of the A solution and 1500 L of the B solution to a semi-batch process where the reactor is charged with 500 L of the A solution at which time the B solution flows into the reactor at a rate of 150 L h-1. In both cases, allow the reaction to proceed to a 95% conversion of B; in the semi-batch system, this may require stopping the flow when the reactor contains 2000 L of solution and allowing it to continue to react as a batch reactor until the desired conversion is reached.
A + B → D (1)
2 B → U (2)

## Slide 7: Activity 32.1
In class, we will not perform the batch reactor analysis
  Doing so, one finds
    651 minutes are required to reach 95% conversion of B in a batch reactor
    At the end of the batch process there are 3.2 moles of D per mole of U
Here, we will begin with the analysis of semi-batch operation
Before beginning the analysis of semi-batch operation, mentally perform a qualitative analysis and predict whether (a) the semi-batch processing will take more or less time than batch processing and (b) whether the final selectivity in semi-batch processing will be larger or smaller than that in batch processing

## Slide 8: Activity 32.1
In class, we will not perform the batch reactor analysis
  Doing so, one finds
    651 minutes are required to reach 95% conversion of B in a batch reactor
    At the end of the batch process there are 3.2 moles of D per mole of U
Here, we will begin with the analysis of semi-batch operation
Before beginning the analysis of semi-batch operation, mentally perform a qualitative analysis and predict whether (a) the semi-batch processing will take more or less time than batch processing and (b) whether the final selectivity in semi-batch processing will be larger or smaller than that in batch processing
  By adding a reactant slowly over time, the concentration of that reactant will be low at all times.
    This will cause the rate to be low and therefore it will take longer to reach a given conversion than a batch reactor would
    Keeping the concentration of B low at all times will have a greater effect on the undesired reaction (second order in B) than the desired reaction (first order in B), so the selectivity will be greater than a batch reactor

## Slide 9
Read through the problem statement, and each time you encounter a quantity, write it down and equate it to the appropriate variable
  If there are any additional constant quantities that you know will be needed and that can be calculated from the values given in the problem statement, write the equations needed for doing so

## Slide 10
Read through the problem statement, and each time you encounter a quantity, write it down and equate it to the appropriate variable
  k1 = 8 x 10-3 L mol-1 min-1, k2 = 4 x 10-3 L mol-1 min-1, Vmax = 2000 L, CA,0 = 3 mol L-1, CB,0 = 1 mol L-1, VA,0 = 500 L, = 150 L h-1, fB = 0.95
If there are any additional constant quantities that you know will be needed and that can be calculated from the values given in the problem statement, write the equations needed for doing so

## Slide 11
Read through the problem statement, and each time you encounter a quantity, write it down and equate it to the appropriate variable
  k1 = 8 x 10-3 L mol-1 min-1, k2 = 4 x 10-3 L mol-1 min-1, Vmax = 2000 L, CA,0 = 3 mol L-1, CB,0 = 1 mol L-1, VA,0 = 500 L, = 150 L h-1, fB = 0.95
If there are any additional constant quantities that you know will be needed and that can be calculated from the values given in the problem statement, write the equations needed for doing so
Generate the design equations needed to model the semi-batch reactor by simplification of the general design equations found in Unit 32 or on the AFCoKaRE Exam Handout

## Slide 12
General form of the mole balance design equation:
  Here, 2 reactions so summation expands to 2 terms
  Only B flows in or out of the reactor, so ṅA = ṅD = ṅU = 0
Determine whether the design equations can be solved once, covering the entire semi-batch process, or whether they will need to be solved in stages
  If they need to be solved in stages, identify the beginning and end of each stage

## Slide 13
General form of the mole balance design equation:
  Here, 2 reactions so summation expands to 2 terms
  Only B flows in or out of the reactor, so ṅA = ṅD = ṅU = 0
Determine whether the design equations can be solved once, covering the entire semi-batch process, or whether they will need to be solved in stages
  If they need to be solved in stages, identify the beginning and end of each stage
    Stage 1 (semi-batch): starts when flow of B into the reactor starts; ends when flow of B into the reactor ends
    Stage 2 (batch): starts immediately after stage 1 ends, ends when the conversion of B reaches 95%

## Slide 14
General form of the mole balance design equation:
  Here, 2 reactions so summation expands to 2 terms
  Only B flows in or out of the reactor, so ṅA = ṅD = ṅU = 0
Determine whether the design equations can be solved once, covering the entire semi-batch process, or whether they will need to be solved in stages
  If they need to be solved in stages, identify the beginning and end of each stage
    Stage 1 (semi-batch): starts when flow of B into the reactor starts; ends when flow of B into the reactor ends
    Stage 2 (batch): starts immediately after stage 1 ends, ends when the conversion of B reaches 95%
  If ṅB is set equal to zero in stage 2, the same equations can be used for both stages

## Slide 15
For each stage of the solution, identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations

## Slide 16
For each stage of the solution, identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations
  Solving the equations will yield the values of t, nA, nB, nD and nU at the end of the stage
Assuming that the semi-batch reactor design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values for each stage of the solution

## Slide 17
For each stage of the solution, identify the specific set of equations that needs to be solved and within those equations identify the independent and dependent variables, if appropriate, and the unknown quantities to be found by solving the equations
Assuming that the semi-batch reactor design equations will be solved numerically, specify the information that must be provided and show how to calculate any unknown values for each stage of the solution
  Initial conditions
    values of independent and dependent variables at start of each stage
  Final conditions
    stage 1: time that addition of B ends
    stage 2: moles of B present when conversion reaches 95%
  Code to evaluate f1 through f4 given independent and dependent variables

## Slide 18
Stage 1
  Initial conditions
    t = 0, nA = nA,0, nB = nD = nU = 0
  Final condition
    Flow of B stops when V = Vmax
  Code to evaluate f1 through f4
    Need to first calculate r1 and r2
    Need to calculate CA and CB
Stage 2
  Initial conditions
    equal to final values of t, nA, nB, nD and nU from stage 1
  Final condition
  Code as above
Identify what variables will become known upon solving the design equations and show how those variables can be used to answer the questions that were asked in the problem

## Slide 19
Solving the design equations gives the time for each of the two stages and the final moles of A, B, D and U for each of the two stages
  tsemi = tf,1 + tf,2

## Slide 20: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions