## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 35

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions

## Slide 3: Zoned Reactor Models
Used when a reactor does not quite satisfy the assumptions of an ideal reactor model
Treat that reactor as if it contains different zones
  Each zone behaves like an ideal reactor
  The zones are connected to form a network
  Adjustable parameters associated with the network can be used to adjust the performance of the zoned model to best match the performance of the actual reactor.
    number of zones
    relative sizes of zones
    fractional splits of network streams
Useful types of zones
  PFR zone
    just like a PFR
  CSTR zone
    just like a CSTR
  Well-mixed stagnant CSTR zone
    like a CSTR except its inlet and outlet are connected at the same point in the zone network
    it draws its feed and returns its product at the same point in the network

## Slide 4: Questions?

## Slide 5
A tube that is 6 m long with an inside diameter of 7 cm is packed with pellets of solid catalyst. Reaction (1) takes place within this reactor at a constant temperature of 450 ºC and a constant pressure of 5 atm. The reactor will be fed 200 ft3 h-1 of a gas containing 15% A, 15% B and 70% I (an inert gas). Reaction (1) is one-half order in A and first order in B. Suppose that the packing in the tube is not uniform, and as a consequence 5% of the bed has a lower density (leading to a rate coefficient of 59.5 mol h-1 atm-0.5 m-3), while the remainder has a higher density (with a rate coefficient of 72 mol h-1 atm-0.5 m-3). Using a zoned reactor model with a well-mixed stagnant zone 3 m into the reactor representing the lower density region and modeling the remainder of the reactor as a PFR, calculate the conversion if 15% of the flow in the PFR is diverted to the well-mixed stagnant zone.
2 A + B → 2 Z (1)

## Slide 6: General Approach to Reactor Network Problems
Read through the problem statement and make a sketch of the network in which each flow stream, reactor, stream split and stream merge is labeled
Read through the problem statement a second time and (a) assign each quantity given in the problem statement to the appropriate variable symbol (b) choose a basis, if necessary and (c) determine what quantities the problem asks for and assign appropriate variable symbols to them
Write the design equations for each reactor in the network following the General Approach to Solving Quantitative Reaction Engineering Problems
If the design equations for any of the individual reactors can be solved at this point, do so and then repeat this step
Write mole and energy balances for each stream split and for each stream merge and solve any that can be solved
If the design equations for any of the individual reactors can be solved at this point, do so and then repeat this step
Solve all of the remaining equations simultaneously or, if possible, group them into sets that can be solved independently and solve each set
After the all of the equations have been solved, use the results to calculate any other requested quantities or plots

## Slide 7: General Approach to Reactor Network Problems
Read through the problem statement and make a sketch of the network in which each flow stream, reactor, stream split and stream merge is labeled
  Recall from today’s informational reading, these two diagrams are completely equivalent
  I’ve labeled the flow streams, stream split and stream merge so everyone will have the same notation

## Slide 8: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions