## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 36

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions

## Slide 3: Segregated Flow Model
Segregated flow models may be useful when the flow in a reactor does not conform to the assumptions of an ideal PFR or CSTR
  They are most easily formulated if the reactor being modeled is isothermal
  They require knowledge or measurement of the age function or the age distribution function
    See Unit 11
Assumptions of the segregated flow models
  The fluid flowing through the reactor is assumed to be composed of very small fluid elements
    The mixing within the fluid elements is referred to as micro-mixing
    Perfect micro-mixing is assumed
  Mixing between fluid elements only occurs at certain times
    Mixing between fluid elements is referred to as macro-mixing
    Two different segregated flow models can be formulated depending upon when the macro-mixing occurs
  The residence times of the fluid elements are not all the same; they are distributed according to the residence time distribution for the reactor being modeled
In the late-mixing segregated flow model, the average conversion is found by integrating over the age distribution function
  Any intensive reactor property, other than the conversion, that depends on the fluid element residence time can be computed in an analogous manner

## Slide 4: Variations on the Segregated Flow Model
Late-mixing segregated flow model
  All of the fluid elements enter the reactor at the same time
  The fluid elements exit the reactor at different times, according to the residence time distribution for the reactor being modeled
  After the fluid elements have all exited the reactor, they macro-mix to yield a uniform composition
  It is equivalent to a PFR with the product removed along its length so that the distribution of fluid element residence times matches the age distribution function
Early-mixing segregated flow model
  All of the fluid elements leave the reactor at the same time
  The fluid elements enter the reactor at different times according to the residence time distribution function for the reactor being modeled
  As soon as a fluid element enters the reactor, it macro-mixes with the fluid elements that are already in the reactor
  It is equivalent to a PFR with the feed distributed along its length so that the distribution of fluid element residence times matches the age distribution function

## Slide 5: Questions?

## Slide 6: Activity 36.1
In Example 36.1, the irreversible elementary reaction in equation (1) occurred isothermally in a non-ideal reactor. At the reactor temperature the reaction was second order in A, and the rate coefficient was equal to 0.5 L mol-1 min-1. The reactor volume was 25 L, and the feed consisted of 4 L min-1 of a solution containing A at a concentration of 2.3 mol L-1. The age function for this reactor had been measured and is given in equation (2). Suppose, instead that reaction (1) is first order with a rate coefficient of 0.7 min-1. Use a late-mixing segregated flow model to compute the conversion in the reactor and compare it to the conversion predicted by the ideal CSTR model.
A → Z (1)
(2)

## Slide 7
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol

## Slide 8
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol
  k = 0.7 min-1, V = 25 L, = 4 L min-1 and CA,feed = 2.3 mol L-1
Read through the problem statement and write down any relationships it provides

## Slide 9
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol
  k = 0.7 min-1, V = 25 L, = 4 L min-1 and CA,feed = 2.3 mol L-1
Read through the problem statement and write down any relationships it provides
Write the equation you will use to model the reactor

## Slide 10
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol
  k = 0.7 min-1, V = 25 L, = 4 L min-1 and CA,feed = 2.3 mol L-1
Read through the problem statement and write down any relationships it provides
Write the equation you will use to model the reactor
Decide how you will solve that equation and determine what you need in order to do so

## Slide 11
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol
  k = 0.7 min-1, V = 25 L, = 4 L min-1 and CA,feed = 2.3 mol L-1
Read through the problem statement and write down any relationships it provides
Write the equation you will use to model the reactor
Decide how you will solve that equation and determine what you need in order to do so
  The equation can be integrated numerically
  An expression for the conversion in a fluid element as a function of its reaction time is needed
  The age distribution function is needed
Generate an expression for the conversion in a fluid element as a function of its residence (reaction) time

## Slide 12
Read through the problem statement and each time you encounter a quantity, assign it to the appropriate variable symbol
  k = 0.7 min-1, V = 25 L, = 4 L min-1 and CA,feed = 2.3 mol L-1
Read through the problem statement and write down any relationships it provides
Write the equation you will use to model the reactor
Decide how you will solve that equation and determine what you need in order to do so
  The equation can be integrated numerically
  An expression for the conversion in a fluid element as a function of its reaction time is needed
  The age distribution function is needed
Generate an expression for the conversion in a fluid element as a function of its residence (reaction) time

## Slide 13
Generate the age distribution function

## Slide 14
Generate the age distribution function
Check that the age distribution function is properly normalized

## Slide 15
Generate the age distribution function
Check that the age distribution function is properly normalized
  it is
Substitute in the late-mixing segregated flow model equation and solve for the conversion

## Slide 16
Generate the age distribution function
Check that the age distribution function is properly normalized
  it is
Substitute in the late-mixing segregated flow model equation and solve for the conversion
  The conversion is 81.4%
Compare to the conversion predicted by the ideal CSTR model and comment

## Slide 17
Generate the age distribution function
Check that the age distribution function is properly normalized
  it is
Substitute in the late-mixing segregated flow model equation and solve for the conversion
  The conversion is 81.4%
Compare to the conversion predicted by the ideal CSTR model and comment
  The conversion is 81.4%
  Using the segregated flow model with an ideal CSTR age function leads to a different conversion than using the ideal CSTR model except when the kinetics are first order

## Slide 18: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions