## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 37

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions

## Slide 3: Reactors Other Than CSTRs and PFRs
When reactants and/or products are present in two or more phases in a reactor, it is generally necessary to write mole and energy balances on each phase
In some cases simple stirred tanks or tubular packed beds are used for multi-phase reactions
In other cases, more specialized reactors are used
  For gas-solid or solid-catalyzed gas phase reactions
    fluidized bed reactors
    riser reactors
  For solid-catalyzed gas-liquid reactions
    trickle bed reactors
    slurry reactors (also for solid-catalyzed liquid reactions)
  For gas-liquid reactions
    spray tower reactors
    bubble column reactors
  Combined reaction and separation
    Reactive distillation columns
    Membrane reactors
  Laminar flow reactors

## Slide 4: Questions?

## Slide 5
A gas mixture containing CO2 is fed to an isothermal, steady state CSTR. A solution containing an amine, NH2R, is also fed to the reactor. The agitator system for the reactor has been designed so that the gas phase may be treated as perfectly mixed. The gas is dispersed as bubbles in the liquid, which is also perfectly mixed. The inlet molar flow rates of all species are known and constant, as are the liquid volume, the gas volume and the interfacial area per volume of liquid, AV. The inlet and outlet volumetric flow rates may be taken to be equal and known. None of the gases except CO2 are soluble in the solution, and none of the components of the solution are volatile. When CO2 dissolves in the solution, it reacts with the amine to form an adduct according to equation (1). The rate expression for the reaction is given in equation (2) where square brackets denote solution phase concentrations, and the rate coefficient is known. If the reaction rate is very, very slow, then the gas phase and solution phase CO2 will be equilibrated according to Henry’s Law, equation (3), where h is the known Henry’s law constant. Write the mole balance design equations needed to calculate the amount of CO2 removed from the gas phase by this reactor.
NH2R + CO2 → CO2:NH2R (1)
(2)
(3)

## Slide 6: Solution
How many sets of design equations will be needed?

## Slide 7: Solution
How many sets of design equations will be needed?
  There are two phases and reactants and/or products are present in both phases, so two sets of design equations will be needed
What are the two sets of design equations for?

## Slide 8: Solution
How many sets of design equations will be needed?
  There are two phases and reactants and/or products are present in both phases, so two sets of design equations will be needed
What are the two sets of design equations for?
  One set for the gas phase and one set for the liquid phase
What design equations will be needed for the gas phase?

## Slide 9: Solution
How many sets of design equations will be needed?
  There are two phases and reactants and/or products are present in both phases, so two sets of design equations will be needed
What are the two sets of design equations for?
  One set for the gas phase and one set for the liquid phase
What design equations will be needed for the gas phase?
  The reactor is isothermal, so the mole balance design equations can be solved independently of the energy balance
  In this problem, energy balances will not be needed to answer the question
  Only mole balances are needed
  The only reactant or product in the gas phase is CO2, so a mole balance on CO2 is needed.
What assumptions can we make about the gas phase when writing its mole balance?

## Slide 10: Solution
How many sets of design equations will be needed?
  There are two phases and reactants and/or products are present in both phases, so two sets of design equations will be needed
What are the two sets of design equations for?
  One set for the gas phase and one set for the liquid phase
What design equations will be needed for the gas phase?
  The reactor is isothermal, so the mole balance design equations can be solved independently of the energy balance
  In this problem, energy balances will not be needed to answer the question
  Only mole balances are needed
  The only reactant or product in the gas phase is CO2, so a mole balance on CO2 is needed.
What assumptions can we make about the gas phase when writing its mole balance?
  It is perfectly mixed, so we can write the mole balance by analogy to the CSTR design equations, except there will be an additional net input term
  The reactor is at steady state, so we do not need accumulation terms
  The second reactant is not present in the gas phase, so there is no reaction (generation) term
Write the mole balance on CO2 for the gas phase

## Slide 11: Solution
How many sets of design equations will be needed?
  There are two phases and reactants and/or products are present in both phases, so two sets of design equations will be needed
What are the two sets of design equations for?
  One set for the gas phase and one set for the liquid phase
What design equations will be needed for the gas phase?
  The reactor is isothermal, so the mole balance design equations can be solved independently of the energy balance
  In this problem, energy balances will not be needed to answer the question
  Only mole balances are needed
  The only reactant or product in the gas phase is CO2, so a mole balance on CO2 is needed.
What assumptions can we make about the gas phase when writing its mole balance?
  It is perfectly mixed, so we can write the mole balance by analogy to the CSTR design equations, except there will be an additional net output term
  The reactor is at steady state, so we do not need accumulation terms
  The second reactant is not present in the gas phase, so there is no reaction (generation) term
Write the mole balance on CO2 for the gas phase

## Slide 12
What design equations will be needed for the liquid phase?

## Slide 13
What design equations will be needed for the liquid phase?
  Again, an energy balance is not needed
  There are two reactants and one product, mole balances can be written for each of these three species
What assumptions can we make about the liquid phase when writing its mole balances?

## Slide 14
What design equations will be needed for the liquid phase?
  Again, an energy balance is not needed
  There are two reactants and one product, mole balances can be written for each of these three species
What assumptions can we make about the liquid phase when writing its mole balances?
  As with the gas phase, it is perfectly mixed, so we can model the equations after the CSTR design equations, except for CO2 there will be an extra net input term
  The reactor is at steady state, so there are no accumulation terms
Write the mole balances for the liquid phase

## Slide 15
What design equations will be needed for the liquid phase?
  Again, an energy balance is not needed
  There are two reactants and one product, mole balances can be written for each of these three species
What assumptions can we make about the liquid phase when writing its mole balances?
  As with the gas phase, it is perfectly mixed, so we can model the equations after the CSTR design equations, except for CO2 there will be an extra net input term
  The reactor is at steady state, so there are no accumulation terms
Write the mole balances for the liquid phase
Determine the type of the design equations and what will be needed to solve them numerically

## Slide 16
What design equations will be needed for the liquid phase?
  Again, an energy balance is not needed
  There are two reactants and one product, mole balances can be written for each of these three species
What assumptions can we make about the liquid phase when writing its mole balances?
  As with the gas phase, it is perfectly mixed, so we can model the equations after the CSTR design equations, except for CO2 there will be an extra net input term
  The reactor is at steady state, so there are no accumulation terms
Write the mole balances for the liquid phase
Determine the type of the design equations and what will be needed to solve them numerically
  The design equations are a set of four non-linear algebraic equations
  They can be solved numerically for four unknowns
  To do so one must provide
    guesses for the values of the unknowns
    code that is given values for the unknowns and uses those values to evaluate the left hand sides of the four equations above
Show how to solve the design equations by providing the necessary info

## Slide 17
  To do so one must provide
    guesses for the values of the unknowns
    code that is given values for the unknowns and uses those values to evaluate the left hand sides of the four equations above
Show how to solve the design equations by providing the necessary info
  The following quantities are known according to the problem statement: Vl, AV, ṅ0CO2,g, k, ṅ0NH2R,l
  Thus, the following quantities are unknown: ṅCO2,g, N, ṅCO2,l, [NH2R], [CO2], ṅNH2R,l and ṅCO2:NH2R,l
  We cannot choose any 4 unknowns to be solved for numerically
    The liquid and gas phase amounts of CO2 are not independent; they are related by Henry’s law
    The liquid phase concentrations are related to the outlet liquid molar flow rates
  Therefore, choose to solve the design equations for ṅCO2,g, N, ṅNH2R,l and ṅCO2:NH2R,l
    We must provide guesses for these four unknowns
    We must provide code that uses the value of these four unknowns to evaluate the equations above
    That code, then, must calculate ṅCO2,l, [NH2R] and [CO2]

## Slide 18
  Calculation of [NH2R]
  Calculation of [CO2]
  Calculation of
Show any additional calculations that will need to be performed after the design equations have been solved

## Slide 19
  Calculation of [NH2R]
  Calculation of [CO2]
  Calculation of
Show any additional calculations that will need to be performed after the design equations have been solved
  The values of the four unknowns will be known
  They can be used to calculate the three quantities above
  The amount of CO2 removed, in moles per time, can be calculated either of two ways
    It will equal ṅCO2,l + ṅCO2:NH2R,l
    Or, it will equal ṅ0CO2,g - ṅCO2,g
The assumption of equilibrium between the bulk liquid and bulk gas phase CO2 greatly simplified the necessary equations
  Essentially it assumed that the rate of dissolution of CO2 in the liquid was instantaneous
  Form small groups and discuss how you think the physics of the problem (or the equations needed to solve it) would change if the rate of reaction and the rate of dissolution were comparable
  Unit 39 considers this very issue

## Slide 20: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions