## Slide 1: A First Course on Kinetics and Reaction Engineering
Class 37

## Slide 2: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions

## Slide 3: Reactors Other Than CSTRs and PFRs
When reactants and/or products are present in two or more phases in a reactor, it is generally necessary to write mole and energy balances on each phase
In some cases simple stirred tanks or tubular packed beds are used for multi-phase reactions
In other cases, more specialized reactors are used
  For gas-solid or solid-catalyzed gas phase reactions
    fluidized bed reactors
    riser reactors
  For solid-catalyzed gas-liquid reactions
    trickle bed reactors
    slurry reactors (also for solid-catalyzed liquid reactions)
  For gas-liquid reactions
    spray tower reactors
    bubble column reactors
  Combined reaction and separation
    Reactive distillation columns
    Membrane reactors
  Laminar flow reactors

## Slide 4: Questions?

## Slide 5
A gas mixture containing CO2 is fed to an isothermal, steady state CSTR. A solution containing an amine, NH2R, is also fed to the reactor. The agitator system for the reactor has been designed so that the gas phase may be treated as perfectly mixed. The gas is dispersed as bubbles in the liquid, which is also perfectly mixed. The inlet molar flow rates of all species are known and constant, as are the liquid volume, the gas volume and the interfacial area per volume of liquid, AV. The inlet and outlet volumetric flow rates may be taken to be equal and known. None of the gases except CO2 are soluble in the solution, and none of the components of the solution are volatile. When CO2 dissolves in the solution, it reacts with the amine to form an adduct according to equation (1). The rate expression for the reaction is given in equation (2) where square brackets denote solution phase concentrations, and the rate coefficient is known. If the reaction rate is very, very slow, then the gas phase and solution phase CO2 will be equilibrated according to Henry’s Law, equation (3), where h is the known Henry’s law constant. Write the mole balance design equations needed to calculate the amount of CO2 removed from the gas phase by this reactor.
NH2R + CO2 → CO2:NH2R (1)
(2)
(3)

## Slide 6: Where We’re Going
Part I - Chemical Reactions
Part II - Chemical Reaction Kinetics
Part III - Chemical Reaction Engineering
Part IV - Non-Ideal Reactions and Reactors
  A. Alternatives to the Ideal Reactor Models
    33. Axial Dispersion Model
    34. 2-D and 3-D Tubular Reactor Models
    35. Zoned Reactor Models
    36. Segregated Flow Models
    37. Overview of Multi-Phase Reactors
  B. Coupled Chemical and Physical Kinetics
    38. Heterogeneous Catalytic Reactions
    39. Gas-Liquid Reactions
    40. Gas-Solid Reactions