## Slide 1: Numerical Solution of Initial Value ODEs
Sets of initial value ODEs
  Critical distinction - value of every dependent variable is known at the same value of the independent variable (t0)
  Also know the “final” value of t or one of the zi; solve for the corresponding unknown values of all the other variables
Approach
  Approximate the zi over a small range of t from t0 to t0 + h using a convenient mathematical function (e. g. linear)
  Approximate constants in the chosen mathematical function (e. g. slope in a linear function) using the equations being solved
  Calculate the values of the zi at t = t0 + h using the approximate equations
  Use the result as the new value of t0 and repeat many times until t or zi reaches its known “final” value

## Slide 2: Numerical Solution of Initial Value ODEs
Known Issues
  Generally the smaller the “step size,” h, the greater the accuracy
    but if h becomes too small, numerical roundoff will introduce significant errors
  Stiff ODEs
    One dependent variable changes very abruptly over a very small range of the independent variable
    The changes in that variable affect the changes in other dependent variables over a much larger range of the independent variable
Many different variations on the approach
  Runge-Kutta is arguably the most popular for non-stiff equations
  Special methods are required when solving stiff equations
MATLAB provides several different built in functions
  ode45 can be used for non-stiff equations; it implements the Runge-Kutta method
  ode15s can be used of stiff equations
  By default the built in solvers assume that the final value of t is known
    An additional termination criterion can be specified where the equations are solved until one of the zi reaches a known final value
      A final value of t still must be specified
      zi must reach its final value before t reaches the final value specified for it
Template files named SolvIVDifI.m and SolvIVDifD.m are provided with instructions for their use
  SolvIVDifI.m when the final value of independent variable is known
  SolvIVDifD.m when the final value of one of the dependent variables is known