## Slide 1: Numerical Solution of Boundary Value ODEs
Identification of boundary value ordinary differential equations (ODEs)
  No partial derivatives
  All ordinary derivatives with respect to the same independent variable
  Independent variable ranges from some known lower limit to a different upper limit
    some boundary conditions apply at the lower limit and other boundary conditions apply at the upper limit
Requirements imposed by the MATLAB solver, bvp4c
  Higher order ODEs reduced to sets of first order ODEs
  Each ODE written in the form
    Sij equal zero or constant
To convert any second order ODE into a set of two first order ODEs
  Define a new variable that is equal to the first derivative of the original dependent variable with respect to the independent variable
    This definition becomes one of the two first order ODEs in the set
  In the original second order ODE
    Replace any occurrence of the second derivative of the original dependent variable with the first derivative of the new variable
    Replace any occurrence of the first derivative of the original dependent variable with the new variable
  In the boundary conditions, replace the first derivative of the original dependent variable with the new variable

## Slide 2: Using the MATLAB Template Files
Convert all second order ODEs into sets of two first order ODEs
If the range of valid values of the independent variable starts (or ends) at zero, determine whether any of the the ODEs contain a term of the form Sijyj/x where Sij is a constant
  If not, the ODEs can be solved using the template file SolvBVDif.m
  If so, the ODEs can be solved using the template file SolvBVDifS.m
Modify the appropriate template file as described in the step-by-step instructions for that template file and execute it
  A single guess for each yi is required; think of it as the average value of yi over the whole range of x
  The boundary conditions are entered in the form of residuals or errors
    Arguments to the function bvs are column vectors containing y_at_start and y_at_end
    If the boundary condition for yi is that yi(x=a) = yia, the residual is y_at_start[i] - yia
    If the boundary condition for yi is that yi(x=b) = yib, the residual is y_at_end[i] - yib
See the MATLAB documentation if difficulties are encountered